## Slide 1: Proposal for NR down-scoping: RAN2 aspects
LG Electronics
3GPP TSG RAN Meeting #77 RP-172007
Sapporo, Japan, September 11 - 14, 2017
Agenda item: 9.2.1

## Slide 2: RAN2 situation
Flood of documents submitted to RAN2 (excluding UMTS)
  RAN2 cannot accommodate such amount of documents in the meeting time.
  Only a few documents are treated, and lots of issues are still open.
  It is quite challenging that RAN2 can complete the NR WI until December 2017.
Proposal
  RAN2 focus on features essential for EN-DC until December 2017.
  Deprioritize features listed in the next two slides.
Chart: 
| NR#1 | #97 | #97bis | #98 | NR#2 | #99
 | 615 | 1143 | 1212 | 1681 | 1095 | 1913

## Slide 3: Potential deprioritized features in RAN2
Packet duplication
  No packet duplication in UL
  DL packet duplication can be supported by network implementation (No UE impacts are foreseen)
Support for multiple numerologies
  A UE is configured with only one numerology.
    Impacts to LCP, SR, DRX, etc. could be minimized.
  The gNB can configure multiple numerologies to multiple UEs, one for each.
RA parameter differentiation
  Single RA parameter is used similar to LTE.
MAC with multi-beam operation
  Beam operation is invisible to MAC functions, e.g. PHR, RA.
Data transmission in RRC_INACTIVE
  Data transmission/reception is allowed only in RRC_CONNECTED.

## Slide 4: Potential deprioritized features in RAN2
Temporary UE capability
  Not essential for NR phase I.
RLF with beam recovery
  LTE RLF mechanism is reused in NR.
CSG
  No active discussion in RAN2 so far.
Slicing
  No active discussion in RAN2 so far.
Connection to 5GC
  First priority is given to connection to EPC.
NR standalone operation (including handover)
  SA related issues can be discussed after NSA issues are completed.