## Slide 1: Supporting 2Tx UE and Single UL Transmission in NR
RAN#77, SAPPORO, JAPAN SEPTEMBER 11-14 2017 RP-172020 AI 9.2.1
AT&T

## Slide 2: Motivation
Dual connectivity between LTE and NR is a key feature used by the Option 3X NSA architecture. This requires separate UL transmission on the MCG and SCG to deliver the UCI independently to each one of them.
    UL PUCCH on SCG and MCG delivers the HARQ ACK/NACK, CSI measurements
    UL PUSCH on SCG and MCG allows for the UL bearer to be split.
In some band combinations such as NR on 3.5GHz and LTE on 2GHz there is potential issue of supporting simultaneous UL on both bands due to inter-mod between these two bands.
    Even for these band combinations the problem only happens when the transmit power in both or one of these bands is high. When the transmit power in both of these bands is low then the problem is mitigated significantly and it is possible to sustain simultaneous UL transmission on both the bands
This contribution highlights potential techniques and their pros and cons for addressing this issue.

## Slide 3: Observations on UE operation
Observation 1: When a UE operates using dual connectivity between LTE and NR it is expected to transmit on both the UL carriers simultaneously.
Observation 2: In certain band combinations between LTE and NR transmitting on both the carriers in the UL can lead to potential degradation in performance due to inter-mod issues.

## Slide 4: Proposals
Proposal 1: For LTE-NR dual connectivity the baseline operation assumes the UE to be capable simultaneous transmission on both the UL carriers.
Proposal 2: For certain band combinations and scenarios which results in Rx MSD issues from simultaneous transmission on both the UL carriers, the UE is expected to transmit on only 1 UL carrier at any given time.
Proposal 3: UE indicates to the network for a given band combination if is suffers from Rx MSD issues while transmitting on both the UL carriers simultaneously.
Proposal 4: RAN plenary should send LS to the various RAN WG to identify the band combinations and enable this use case for LTE-NR dual connectivity where the UE is able to transmit on only one UL carriers at a time
Proposal 5: The Network then makes the final decision and indicates to the UE whether or not it should transmit on both the UL carriers simultaneously for that given band combination.