## Slide 1: New WI on Separation of CP and UP for Split Option 2
Tdoc: RP-172310
Agenda Item: 9.1.3

## Slide 2: Background (1/2)
RAN3 carried out a study on separation of NR control plane (CP) and user plane (UP) for split option 2. The outcome of the study is summarized in the following:
  Three scenarios for the separation of CU-CP and CU-UP were identified:
    Scenario 1: CU-CP and CU-UP centralized;
    Scenario 2: CU-CP distributed and CU-UP centralized;
    Scenario 3: CU-CP centralized and CU-UP distributed;
    Benefits and drawbacks have been analyzed and each scenario has proven to be beneficial to support different types of services and to satisfy different network requirements. It can be concluded that the CU-CP and CU-UP separation allows to optimally address the different requirements coming from future 5G services.
    The separation of CU-CP and CU-UP allows to scale different functions independently and to take maximum advantage of cloud and virtualization technologies that are a key component of 5G systems.
  Two solutions for the separation of CU-CP and CU-UP were discussed:
    Separation of CU-CP and CU-UP by implementation;
    Standardisation of an open interface;
    The standardisation of an open interface favors multi-vendor interoperability.
    It was concluded that the definition of an open interface is feasible and beneficial.

## Slide 3: Background (2/2)
RAN3 carried out a study on separation of NR control plane (CP) and user plane (UP) for split option 2. The outcome of the study is summarized in the following:
  The design of an open interface between CU-CP and CU-UP (namely E1) was performed including:
    Definition of the architecture and general principles of the E1 interface;
    Definition of the basic functions and procedures of the E1 interface;
    The E1 interface does not affect the work on the other interfaces for which RAN3 is responsible.
    The current NG-RAN architecture is already designed to support the CU-CP and CU-UP separation.

## Slide 4: Work Item description
The objective of this work item is to continue and complete the specification of the E1 interface between CU-CP and CU-UP in RAN3 (based on TR 38.806).
  Finalize the specification of the E1 general principles, functions, and procedures:
    It includes the selection of a mechanism for security activation and configuration (with confirmation from SA3);
    It includes the description of all the E1 functions and procedures;
    The outcome is to be collected e.g., in a TS 38.4x0 specification.
  Specification of the E1 signalling transport:
    It is based on the use of the SCTP/IP protocol stack,
    The outcome is to be collected e.g., in a TS 38.4x2 specification.
  Specification of the E1 application protocol (E1AP):
    The E1AP includes the stage-3 description of the E1 elementary procedures and messages;
    The outcome is to be collected e.g., in a TS 38.4x3 specification.