## Slide 1: 3GPP TSG RAN Meeting #78 Lisbon, Portugal, December 18-21, 2017 Agenda item: 9.1 Document for: Discussion
IoT Evolution in Rel-16
RP-1702393

## Slide 2: IoT : Roadmap in 3GPP
Rel-13 eMTC
1.4 MHz bandwidth
One deployment scenario: in-band
Max data rate(FD-FDD):
~800 kbps/~1 Mbps
Coverage enhancement: 155.7dB
Rel-13 NB-IoT
180 kHz bandwidth
Three deployment scenarios: In-band, guard-band, standalone
Max data rate(anchor, inband):
~22.6 kbps/ ~58.3 kbps
Coverage enhancement: 164 dB
Rel-14 eMTC
Up to 5 MHz bandwidth BL UE
Large TBS support
Max data improvement
Positioning : OTDOA
Multicast support
VoLTE enhancement
Rel-14 NB-IoT
Positioning : OTDOA
Multicast support
Non-Anchor PRB support
New power class
Max data rate((anchor, inband):
~65.1 kbps/~142.5 kbps
Rel-15 eMTC
Power consumption ,latency, system acquisition time, load control
Spectrum efficiency
Support of higher UE velocity
Rel-15 NB-IoT
Power consumption ,latency, system acquisition time, load control
TDD
Small cell
Measurement accuracy enhancement
IoT Evolution

## Slide 3: Further IoT evolution in Rel-16
Guideline in Rel-16 IoT work:
System efficiency enhancement
Coverage extension enhancement
Positioning enhancement
TDD NB-IoT enhancement
Operator will be able to leverage existing eMTC/NB-IoT investment

## Slide 4: System efficiency enhancement for eMTC
Enhancement of standalone eMTC
  Supported bandwidth
  Removal of reserved legacy PDCCH area will allow more capacity improvement
  Control channel MPDCCH narrowband (1.4Mhz) support
Dynamic HARQ timing for eMTC
  Current pre-configured UL/DL HARQ timing negatively impacts system scheduling performance
Multi-subframe scheduling support for eMTC
  Further reduction in control overhead

## Slide 5: System efficiency enhancement for NB-IoT
NB-IoT DL PDSCH performance enhancement
  Improvement for high data rate performance
Cross-carrier scheduling support
Multi-subframe scheduling support
  Further reduction in control overhead

## Slide 6: System efficiency enhancement for NB-IoT cont.
Inter-cell interference enhancement for NB-IoT
  NRS enhancement
  NPUSCH scrambling
  NPRACH interference reduction
Comparison of NPUSCH performance
ALT1 :Legacy
ALT2: Enhanced

## Slide 7: Coverage Extension Enhancement
Small portion of the deployed UE in deep coverage hole
Existing coverage extension methods still cost heavy power consumption
Coverage can be extended via in-coverage UE
  Multi-hop/Single-Hop in-band Relay
    Minimize legacy network impact
    Considering different relay node scenario

## Slide 8: Positioning enhancement
Positioning enhancement
  Rel-14 eMTC/NB-IoT only supports basic OTDOA positioning functions. However, the bandwidth of the NPRS/PRS limits the accuracy that can be achieved (50m legacy requirement).
  UTDOA support
  Postionion accuracy improvement
  Positioning power consumption improvement

## Slide 9: TDD enhancement for NB-IoT
In Rel-15 TDD NB-IoT, target is to support the same features as Rel-13 NB-IoT, additionally considering small-cells scenarios
  However, Rel-14/Rel-15 NB-IoT has gone through considerable improvement
TDD enhancement in Rel-16
  Early data transmission (EDT) support
  Wake-up signal support
  Multi-cast support
  HARQ feedback early termination

## Slide 10: Thank you