## Slide 1
Motivation for new WI proposal on uplink data compression in UMTS
www.huawei.com
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18-21, 2017
Agenda Item: 11.1
Huawei, HiSilicon
RP-172443
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Scenario and requirements
Compared to downlink, uplink data transmission efficiency is more challenging. So far, lots of methods have been standardized, but most of them focus on radio aspects, e.g. Dual Cell HSUPA. For some services, e.g. web surfing, FTP traffic, in order to achieve compression efficiency, some means in PDCP layer could be considered.
Currently, there is an ongoing LTE WI UDC (Uplink Data Compression) and this WI is to be completed by RAN#79 (March 2018). In the WID, it shows significant gains brought by UDC.
  RAN2 agreed on the performance evaluation criteria of compression efficiency. The simulation results of UDC solution based on DEFLATE (solution 3) and Solution 4 (APDC) have shown a similar trend in terms of the compression efficiency for uplink on various input traffic profiles simulated including FTP, SIP signalling, video and web surfing in case 1 and case 2 type traffic scenarios. Wherein, about 40% to 50% compression efficiency is shown for FTP traffic, over 80% of compression efficiency is shown for SIP signalling and about 60% to 75% compression efficiency is shown for video traffic. Similarly, over 60% of compression efficiency can be obtained with web surfing data. Solutions based on DEFLATE and solution based on APDC have shown significant and similar compression efficiency, as concluded in TR 36.754.
UDC, as an compression algorithm, is RAT independent, we believe similar gains could be achieved if DUC could be implemented in UMTS.

## Slide 3
Opportunities of uplink enhancements
In the LTE WI UDC, the DEFLATE-based solution is included. Basically, it is to introduce a compression/de-compression mechanism in PDCP layer in order to reduce the size of uplink data.
For this LTE feature, most of stage-2 and stage-3 aspects have been decided, e.g. new PDCP PDU type, checksum, checksum failure, RRC signallings for activating/de-activating this feature.
In order to simplify the work of UDC in UMTS, normative work which has been done for LTE WI UDC should be considered as a baseline.

## Slide 4
Objective of the WI UDC in UMTS
The objective of this WI is to specify only the DEFLATE-based solution as follows:
  To specify the signaling and procedures enabling operator control of the DEFLATE-based solution.
  To specify the UDC header (at least including checksum) and, PDCP control signaling as necessary, in PDCP protocol.
  To analyze impact of buffer size and authentication when using pre-defined dictionary. And if needed, corresponding signaling and procedure should be specified.
  Note: Normative work which has been done for WI on LTE UDC should be considered as a baseline.

## Slide 5
Copyright©2017 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !