## Slide 1
Motivation for new WI proposal on further enhancements of uplink for LTE
www.huawei.com
3GPP TSG RAN Meeting #78
Lisbon, Portugal, December 18-21, 2017
Agenda Item: 10.1.1
Huawei, HiSilicon
RP-172444
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Scenario and requirements
Diverse uplink dominated applications become more and more popular in existing networks. For example, video monitoring/sharing/meeting/chatting over wireless link has rapidly been developed nowadays especially for Safe City/Village, Smart Home and etc. Such applications typically require high and stable data rate in uplink transmission for stationary UEs, e.g., cameras and CPEs.
Requirements of video monitoring
  Per link (1080P with H. 265 coding): ~2Mbps
  Per link (4K with H.265 coding): ~8Mbps
  Per cell: 140-560Mbps (In some safe city scenario, 70 cameras per cell are needed)
  High and stable data rate in uplink anywhere
  Real time monitoring (always online and activated)

## Slide 3
Challenges of uplink enhancements
In uplink, the maximum transmitting power is usually restricted due to the cost and capability of UEs. According to Shannon capacity theorem, for a given S/n0, the capacity is limited, regardless of the big bandwidth size that can be used.
The current spectrum efficiency of both cell average and cell edge in uplink can hardly meet the requirements of video transmission.
  LTE R10 UL 4x4:
  cell average throughput = 49.6Mbps @20MHz
  cell edge throughput = 1.54Mbps@20MHz
  Restricted MIMO schemes due to the single carrier characteristic in uplink

## Slide 4
Opportunities of uplink enhancements
For safe city and smart home monitoring, the application and environment characteristics should and need to be utilized for uplink enhancements
  Less limitation on device cost, power, size, and processing capabilities
  UEs in such scenarios are typically new type of devices. so it is feasible to introduce more advanced features in LTE uplink
  Stationary UEs with slow-varying channels between UEs and eNBs
  The channels would vary quite slowly for typical deployment scenarios. This characteristic can be utilized to further improve the spectral efficiency by e.g., more accurate channel measurement/scheduling/retransmission, RS overhead reduction and so on
  Continuous traffic with large packet size and usually small inter-packet interval
  This characteristic can be utilized for better link adaptation

## Slide 5
Objectives
Specify enhancements for stationary UEs in uplink (RAN1, RAN2, RAN4)
  Enhanced uplink SU/MU MIMO schemes for the high capacity UEs such as codebook extension, and non-codebook-based precoding. Other enhancement on UL MIMO is not precluded.
  More accurate channel measurement/scheduling/retransmission
  Overhead reduction of uplink reference signals for slow-varying channels
  Overhead reduction of control channels
  Special improvement for to the users with poor link quality
Define the specific requirements for each band for HPUE. (RAN4)
  These include but are not limited to associated regulatory requirements on transmit power levels, unwanted emissions, radiation requirements, etc.

## Slide 6
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !