## Slide 1: On extreme long range coverage
Orange, Huawei
3GPP TSG RAN#78 18-21 December 2017 Lisbon, Portugal | TDoc RP-172497 Agenda Item 10.1.1

## Slide 2: Background
The extreme Long Range deployment scenario [section 6.1.6 in TR38.913] is defined to allow for the provision of services for very large areas with low density of users whether they are humans or machines.

## Slide 3: Background
The scope of this document is to:
  identify service requirements for long range data and voice services
  discuss potential evaluation methodology
  propose solutions which we believe would be valuable to be studied and specified in 3GPP in a future Work Item
We expect this document to provide a starting point for discussion, leading to a work item proposal for LTE in Rel16
More details are available in the document RP-171875, co-sourced by Orange, Huawei, HiSilicon, Nokia, Nokia Shanghai Bell, and submitted at TSG RAN#77

## Slide 4: Service Requirements
Service requirements for Long Range services are taken from 3GPP TS 22.261, section 6.17:
  density up to 2 user/km2
  minimum user throughput of 1Mbps on DL and 100 kbps on UL
  range of up to 100 km
  maximum of [400] ms E2E latency for voice services at the edge of voice coverage

## Slide 5: Observations (1/3) - as in RP-171875
Observation 1: Different channel models will give different path loss under the same coverage distance.
  suitable channel model for long coverage up to 100km needs to be studied further
Observation 2: The existing LTE system cannot fulfill the requirements of 100km coverage based on ITU-RP.1546-5 channel model. Nevertheless independently from the validity of each path loss model, the reality of the field is that environments are generally hilly with large clutter variety. Coverage improvements in such propagation environments are better assessed in dB (MCL) rather than in km (cell ranges).
  To that purpose, it is proposed to set a 20 dB coverage extension target to the existing LTE baseline. This translates into 160.7 dB Maximum Coupling Loss target for Long Range Connectivity Data services.

## Slide 6: Observations (2/3) - as in RP-171875
Observation 3: The system shall support a maximum of [400] ms E2E latency for voice services at the edge of coverage, which cannot be reached with 20 dB path loss improvement
  To cope with that several solutions are envisaged:
    Keep the service requirements for Voice QoS (with a revised requirement to be studied (e.g. « up to 10 dB » path loss improvement)
    Keep the coverage requirement for voice to remain similar to data services (e.g. 20 dB path loss improvement) but accept a substantial degradation of QoS service, leading to “walkie-talkie” type of experience. (i.e. “10s E2E delay”) – However this may not be acceptable.
    Propose a mix of the 2 solutions, with both a reduced coverage and degraded QoS requirements, with target values to be studied further (e.g. “up to 15 dB path loss improvement and 1s E2E delay”)

## Slide 7: Observations (3/3) - as in RP-171875
Observation 4: Studied techniques in eMTC and eVoLTE can be reused and improved to extend the coverage of LTE for Long Range Connectivity services.
  We would like to initiate discussion around these observations, with a view to developing understanding in RAN plenary of the requirements, leading to a new Work Item in due course.

## Slide 8: Further observations
In addition to the previous service requirements from 3GPP TS 22.261 aimed at extreme long range coverage, the following service could also drive the need for extended path loss: SMS support over mode- A and mode-B
  Idea : allow smartphones supporting CE mode A & B to keep at least the ability the send/receive SMS while such an coverage condition that available throughput will not allow voice/data service
  Main application: allow emergency / SOS message, authentication token, payment credential checks, even in locations where there is no regular coverage (e.g. not only in extreme rural but also very deep indoor within urban environments)

## Slide 9: Possible solutions
Current solution
  Coverage enhancements techniques inherited from eMTC (mode A & Mode B) and eVoLTE standardized in Rel14 can already be implemented in an LTE smartphone to extend the coverage of a standard MBB category device (Cat 3 and above)
Possible enhancements
  High Power UE in low bands targeted for coverage (e.g. band 20)
  DL MIMO 2x2 operated with mode A & mode B (with coverage enhancement for CSI reporting)
  Mobility enhancements for mode A & mode B

## Slide 10: Next steps
Propose addition of high power UE in targeted bands (e.g. band 20) within the high power UE basket WI in RAN4 (by Q1 18).
Propose a Rel16 WI to plan the specification of the enhancements suggested in the previous slide. One option is to embed such enhancements within a Rel16 eMTC WI. Target RAN#79 for more discussions, RAN#80 for approval.