## Slide 1: Architecture options in Rel-15
ORANGE, BT, SKT, Telefonica, Telecom Italia
3GPP TSG RAN#78 18-21 December 2017 Lisbon, Portugal | TDoc RP-172627 Agenda Item 9.2.1

## Slide 2: Background 3GPP
As part of the current Rel-15 WI on NR and the LTE evolution to support the new 5GC, multiple architecture options are defined [RP-161266 provides a complete overview]
RP-161266 also asked the question, if all these architecture options need to be defined by 3GPP and how to avoid fragmentation, especially considering roaming ?
RAN#77 confirmed that all architeture options remain part of Rel-15 targeting June 2018 finalisation

## Slide 3: Background Migration
The co-signing operators think that it is important to have planning certainty with regard to migration scenarios and the support of different architectures in terminals. The availibility of support in terminals has implications on details for migration steps as well it might effect the global roaming considerations
Thus we believe it is important to agree on certain aspects regarding the 5G architectures in 3GPP to provide this planning certainty for operators

## Slide 4: Architectures for Migration
The co-signing operators agreed the following architectures* are important along the migration path:
    NSA option 3X
    NSA option 7X
    NSA option 4
    SA option 2
    LTE connected to 5GC via option 5
* the naming of options refers to RP-161266

## Slide 5: Proposal
In order to ensure individual operators migration plans while keeping a unfragmented roaming regime intact, the co-signing operators propose:
Any UE of Rel-15 (June 2018)* – conditioned by its LTE and/or NR support – shall support the following architectures:
2, 3X, 4, 5 and 7X
* UE supporting the early drop (Dec 2017 release) may support only option 3x