## Slide 1: WF on Channel Bandwidth Support for NR
Qualcomm Incorporated, Sprint, Nokia, Nokia Shanghai Bell, Deutsche Telekom, Orange, Telecom Italia, BT, AT&T,
T-Mobile US, Dish Network, Verizon
3GPP TSG-RAN WG4 RAN #78
Lisbon, Portugal, December 18th-21st, 2017
RP-172759

## Slide 2: Background
Agreements in RAN4 on UE Channel Bandwidth
  UE maximum channel bandwidth is a UE capability. (R4-1708845)
  UE shall support any Rel-15 channel bandwidth that is smaller than its UE supported maximum channel bandwidth. (R4-1706321)
  The maximum channel bandwidth supported by UE can be different for UL & DL and SCS specific. (R4-1706321)
  Different maximum channel bandwidths can defined for different SCS (R4-1706321)
    Maximum channel bandwidths for certain SCS can be smaller than the ones listed above but not larger
  UE minimum bandwidth in the context of RMSI and COREST containing PDCCH scheduling RMSI should be no less than 20MHz for Frequency Range 1 and 100MHz for Frequency Range 2 (R4-1714392)

## Slide 3: Signaling Support for Channel Bandwidths
RAN2 should introduce the signaling support for channel bandwidths as following:
  Maximum channel bandwidth supported in each band for DL and UL separately and for each SCS that UE supports
RAN2 should consider that new maximum channel bandwidths could be added in the future and signaling should be forward compatible
RAN2 should consider that new channel bandwidths(lower than maximum defined for the band) could be added in the future and signaling should be forward compatible

## Slide 4: Mandatory Channel BW
For all NR bands below 6 GHz, all bandwidths listed in TS 38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC.
  Channel bandwidths added in future versions will be discussed separately
In the future UE supporting different data rates could be introduced
  Channel bandwidth support will take into account the supported data rate

## Slide 5
NR band / SCS / UE Channel bandwidth |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 101,2 MHz | 152 MHz | 202 MHz | 252 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 100 MHz
n1 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n2 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n3 | 15 | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
n5 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n7 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n8 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n20 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n28 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n38 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n41 | 15 |  | Yes | Yes | Yes |  |  | Yes | Yes |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes
n50 | 15 | Yes | Yes | Yes | Yes |  |  | Yes | Yes |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n51 | 15 | Yes |  |  |  |  |  |  |  |  |  | 
 | 30 |  |  |  |  |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n66 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  | Yes |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  | Yes |  |  |  | 
n70 | 15 | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes | Yes |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes | Yes |  |  |  |  |  | 
n71 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n74 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n75 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
n76 | 15 | Yes |  |  |  |  |  |  |  |  |  | 
 | 30 |  |  |  |  |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n77 | 15 |  | Yes |  | Yes |  |  | Yes | Yes |  |  | 
 | 30 |  | Yes |  | Yes |  |  | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes |  | Yes |  |  | Yes | Yes | Yes | Yes | Yes
n78 | 15 |  | Yes |  | Yes |  |  | Yes | Yes |  |  | 
 | 30 |  | Yes |  | Yes |  |  | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes |  | Yes |  |  | Yes | Yes | Yes | Yes | Yes
n79 | 15 |  |  |  |  |  |  | Yes | Yes |  |  | 
 | 30 |  |  |  |  |  |  | Yes | Yes | Yes | Yes | Yes
 | 60 |  |  |  |  |  |  | Yes | Yes | Yes | Yes | Yes
n80 | 15 | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
n81 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n82 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n83 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  | 
n84 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  |  |  |  | 
NOTE 1: 90% spectrum utilization may not be achieved for 30kHz SCS. NOTE 2: 90% spectrum utilization may not be achieved for 60kHz SCS. |  |  |  |  |  |  |  |  |  |  |  |