## Slide 1
Way Forward on NR EN-DC power sharing capability
RP-172787
3GPP RAN #78
December 18 - 21, 2017
Lisbon, Portugal
Agenda Item 9.2.1
Qualcomm Incorporated

## Slide 2: Background
The discussion in this document assumes that there are two types of NSA UEs supported by the specification:
  UE Type 1 capable of dynamic LTE-NR power sharing
    Converged NR and LTE modem with high speed interface capability
    These UEs can operate with P_LTE + P_NR > P_powerclass configuration or with no P_LTE or P_NR configuration
  UE Type 2 not capable of dynamic LTE-NR power sharing
    Separate NR and LTE modem with limited interface capability
    These UEs can only operate in EN-DC when a configuration is received with P_LTE + P_NR <= P_powerclass
Note that neither type of UEs are allowed to transmit with power above P_powerclass in FR1

## Slide 3: Proposals
Proposal 1
  Agree to introduce Rel-15 capability signaling to indicate whether the UE supports dynamic EN-DC power sharing
    Dynamic power sharing means that the UE can operate with P_LTE + P_NR > P_powerclass configuration
  Agree that the intent is to make dynamic EN-DC power sharing mandatory at a future time
  Check any possible updates on status above in March
Proposal 2
  For UEs without dynamic LTE-NR power sharing capability, the support of single UL operation (Operation A with Case 1 in Slide 5) is mandatory with capability signalling
    Discuss FGI/IoDT issues together with other RAN1 features
Single UL operation (Operation A and Operation B with Case 1 in Slide 5) is optional for dynamic power sharing capable UEs.

## Slide 4
Annex
Qualcomm Incorporated

## Slide 5
Agreements:
  At least for LTE-NR NSA operation
    Maximum allowed power values for LTE (P_LTE) and NR (P_NR) are set separately
      i.e., when UE is configured for NR, P_LTE can be configured up to P_cmax and P_NR can be configured up to P_cmax.
      e.g. P_LTE + P_NR > P_cmax or P_LTE + P_NR = P_cmax
    Signaling details for P_LTE, P_NR are left to RAN2, RAN4.
    Note: ‘P_cmax’ is a limit that is similar to ‘The configured maximum UE output power’ that was specified for LTE.
    Note: The network will still have flexibility to prioritize or reserve certain NR transmission power depending on network implementation
    All UEs are mandated to handle P_LTE + P_NR = P_cmax while handling of P_LTE + P_NR > P_cmax depends on UE capability
    At least, when DL/UL LTE sTTI/reduced UE processing time based operation is not configured for the UE, if total transmit power exceeds P_cmax when there is simultaneous NR and LTE UL tx,
      For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation (note: it is not intended to have RAN4 test from RAN1 perspective)
        If there are two or more UL carriers, the power scaling or tx dropping can be performed for each of the UL carriers separately or jointly up to UE implementation
      For LTE, no change in power control procedure
    FFS the case when DL/UL LTE sTTI/reduced UE processing time based operation is configured for the UE
    The following is FFS
      The case when P_NR is configured such that P_NR < P_cmax, and UE can use power up to P_cmax in NR when it knows that there will be no UL transmission in LTE by semi-static configuration (e.g., measurement gap, DL/UL configuration)

## Slide 6
Agreement:
  For LTE/NR NSA operation,
    If this UE supports dual UL operation and also supports single UL operation with Case 1 HARQ timing, RRC signaling can configure a UE to operate in one of the following modes:
      Dual UL operation
      Single UL operation with Case 1 HARQ timing
      Single UL operation with Case 2 HARQ timing
    For UE supporting single UL operation and with Case 1 HARQ timing if UE does not support power scaling for LTE-NR DC with P_LTE+P_NR>Pcmax, UE shall support the following two operations:
      Operation A with Case1: P_LTE + P_NR > Pcmax, in which case the UE assumes that no NR UL transmission takes place in an UL subframe/slot that is designated as LTE UL in the Case 1 reference TDD configuration
      Operation B with Case1: P_LTE + P_NR <= Pcmax, in which case NR UL can be scheduled in any UL subframe/slot (while the UE behaviour in case of being simultaneously scheduled on LTE and NR uplinks is not specified)
      The operation A vs operation B configuration is implicitly determined based on P_LTE and P_NR
      Note that the above agreement does not affect the current status on the optional/mandatory support of power scaling for LTE-NR DC with P_LTE + P_NR > Pcmax
      Note that the above agreement can become obsolete if power scaling for LTE-NR DC is mandated to all UEs