## Slide 1: UE capabilities and feature deployment phasing for NR
Source: Vodafone
RP-172816
3GPP TSG RAN#78
Lisbon, Portugal, 18th – 21st December 2017

## Slide 2: Background
Discussion on a number of documents on:
  Mandatory and optional features for NR support in devices
  Standardising profiles for parameter configurations to be supported by NR devices for different use cases/frequency bands/deployment scenarios
Discussion demonstrated that there are various reasons why companies would like to make Rel-15 features/parameter configurations (denoted as X below) mandatory or optional for devices:
  1) Initial Access-related: If X is not supported, then initial access may have interoperability issues on day 1
  2) Forward compatibility-related: If X is not supported then, even though it is not a problem on day 1, it may not be feasible to operate X later on due to legacy devices not supporting X, causing:
  a) lack of compatibility between initial and later deployment configurations, or
  b) severe system level performance degradation or restriction in later deployment configurations (i.e. the gains expected from X cannot be achieved due to lack of legacy device support)
  3) Harmonisation-related: If a harmonized configuration of X is not supported by the ecosystem, then there may either not be interoperability across the ecosystem or there may be severe performance degradation, both due to implementation of the same functionality with no alignment in parameter settings supported

## Slide 3: Way forward
The “Initial access-related” and “Forwards compatibility” related issues on the previous slide seem to be clear reasons to make functionality or parameter configurations mandatory in 3GPP specifications.
The “Initial access-related” issue is already being considered within WG (RAN1 at least) discussions.
Proposal:
  It is requested for RAN1 and RAN2 to take into account particularly the “Forwards compatibility-related” issue (as defined in slide 2), in addition to “initial access-related” issue when recommending whether a feature/parameter configuration should be mandatory or optional
  For all features and parameter configurations (independent of whether they are made mandatory or optional) it is requested for RAN1 and RAN2 to highlight whether the “initial access-related” issue or “forwards compatibility-related” issue would be applicable – as this would help RAN plenary final decision-making.