## Slide 1: Consideration on Supporting UDC in NR
CATT, MediaTek Inc.
RP-180232
3GPP TSG RAN WG Meeting #79
Chennai, India, March 19-22, 2018
Document for: Discussion
Agenda Item: 9.2.1

## Slide 2: WI on UDC in LTE
The WI on UDC in LTE is completed 99%.
All CRs (36.300, 36.323, 36.331, 36.306) are endorsed, and will be updated and approved in June.
The main changes are:
  Introduce DEFLATE based UDC solution related configuration;
  Define PDCP PDU formats with UDC header and error notification control PDU;
  Define compression procedure and content of UDC header;
  Support predefined dictionary related capability and configuration.

## Slide 3: Motivation to support UDC in NR
UDC could save more UL resources and reduce transmission latency in LTE which make LTE transmission more efficient, 5G also should provide similar effective transmission;
UDC can improve voice service coverage since it can improve the SIP signalling transmission successfully in the edge of cell, and considering the high frequency 5G used, most cells would be small cells which also have the similar voice coverage issue;
The E-UTRAN connecting to EPC with UDC may has higher throughput than the E-UTRAN connecting to 5GC without UDC. To let 5G better than LTE, supporting UDC in 5G is a good solution.
Saving uplink resource is very important for practical networks.

## Slide 4: Effort to support UDC in NR
UDC related function in LTE can be easily reused in NR, most of changes in PDCP can be copied from LTE.
further work for NR may be mainly on signalling design, including the UDC configuration and capabilities in NR which can refer to what has done in LTE.
Some new scenarios maybe considered: e.g. Split DRB etc.
  If no time, can consider in later release.
Reducing the message size is helpful for uplink coverage vulnerability case.

## Slide 5: Proposals
Proposal 1: supporting DEFLATE based UDC in NR, i.e. reuse LTE UDC algorithm and all specifications with adjustment for NR.
Proposal 2: RAN2 can analyze how to support UDC in NR in Rel-15. If possible, corresponding CRs should be submitted in June.