## Slide 1
Discussion on the necessity of applying 60KHz SCS with ECP for High speed train network
CMCC
3GPP TSG RAN Meeting #79 RP-180308
Chennai, India, March 19 - 22, 2018
Agenda Item: 9.1

## Slide 2: Introduction
Enhancements of NR compared to LTE for high speed scenario :
  Scalable subcarrier spacing for below 6GHz:15KHz, 30KHz, 60KHz
    LTE：15KHz, 350km/h
    NR：30KHz, 60KHz, 500km/h
    If deployment carrier frequency is doubled for NR, e.g. from around 2GHz to approximately around 4GHz, then the ICI caused by by Doppler frequency shift is even larger for NR 30KHz SCS than LTE.
  Additional DMRS symbol
Numerology(combination) should be carefully examined considering high speed user experience
  60KHz SCS will be better than 30KHz if only from SCS point of view, but in the concatenated RRU cell as below that referred from TS36.101 v15.5.0 B.3A (also required in TR38.913), the delay spread maybe special, CP may not be sufficient in 60KHz, but for 30KHz, CP maybe fine while the SCS may not be robust enough
 | LTE | NR
speed,kmh | 350.00 | 500.00
carrier frequency,GHz | 2.00 | 4.00
fd,Hz | 648.15 | 1851.85
SCS，KHz | 15.00 | 30.00
fd/SCS | 0.04 | 0.06

## Slide 3
No consensus in WGs on the benefit of 60kHz and ECP, and no common knowledge about the optimal numerology options for high speed scenarios, at least from existing evaluation results submitted in RAN1, e.g.,
  For high Doppler spread with 300ns or even less delay spread, some results show that 60KHz NCP provides the best performance comparing to 30KHz and 60KHz ECP, while
  For high Doppler spread and larger delay spread, e.g., 1000ns,
    30KHz NCP shows best performance for TDL-C channel
    60KHz ECP shows best performance for TDL-A channel ;
    Beamforming transmission may play key role in numerology selection.
  Since delay spread for high speed UEs may span wide variations in SFN scenario ,evaluations on high Doppler spread with SFN channel show:
    For 30KHz NCP, 60KHz NCP and 60KHz ECP, each of them has respective advantage on differently special positions
Observations from WGs
Notes: TDL-A with 1000 nsec

## Slide 4
Numerology 60kHz is optional and ECP is optional base on the current UE feature list discussion, while no sufficient evaluations from 3GPP on the numerology options for high speed SFN and hence no sufficient guidance for operator deployments
Operators need such kind of information to define corresponding requirements/preference on both the network side and UE side
Proposal
  More comprehensive evaluations and analysis are needed to derive common understanding on the necessity of some certain numerology option for UE served by SFN high speed network, other than some specific locations.
  A RANP SI is built to address this requirements.
General observations and proposal
Notes: TDL-A with 1000 nsec