## Slide 1: 3GPP TSG RAN Meeting #79 Chennai, India, March 19 - 22, 2018 Agenda item: 10.1.1 Document for: Discussion
On Rel-16 NB-IoT
RP-180358

## Slide 2: Further NB-IoT evolution in Rel-16
Guideline in Rel-16 NB-IoT work:
System efficiency enhancement
Power consumption enhancement
Coverage extension enhancement
Positioning enhancement
TDD NB-IoT enhancement
Network maintenance enhancement
Connectivity to 5GC
Operator will be able to leverage existing investment.

## Slide 3: System efficiency enhancement for NB-IoT
NB-IoT DL NPDSCH performance enhancement
  Improvement for high data rate performance
Cross-carrier scheduling support
  Reduce blocking in scheduling
Multi-subframe scheduling support
  Further reduction in control overhead
Uplink HARQ-ACK feedback early termination
  Power consumption reduction and improvement for UL spectral efficiency

## Slide 4: System efficiency enhancement for NB-IoT cont.
Inter-cell interference enhancement for NB-IoT
  NRS enhancement
  NPUSCH scrambling
  NPRACH interference reduction
Comparison of NPUSCH performance
ALT1 :Legacy
ALT2: Enhanced

## Slide 5: Further power consumption enhancement
SC-PTM enhancement
  Reduce redundant reception on UE and unnecessary power consumption due to repetition without feedback or without differentiation for the first time transmission and the repeated ones.
RRC connected and idle mode power consumption enhancement
  Connected mode NPDCCH detection optimization.
  Reduce idle state power consumption with enhancement on paging , i.e., with additional consideration on static or semi-static UEs, or with trade-off between paging reliability and minimum repetition numbers.
  Reduce idle mode power consumption for mobility measurement, i.e, measurement optimization for mobility UE.

## Slide 6: Coverage Extension Enhancement
Target small portion of the deployed UE in deep coverage hole and low power class UE
  Existing coverage extension methods still cost heavy power consumption.
Coverage can be extended via in-coverage relay node
  Focus single-Hop Relay
    Minimize legacy network impact
    Considering different relay node scenario

## Slide 7: Positioning enhancement
Rel-14 NB-IoT only supports basic OTDOA positioning functions. However, the bandwidth of the NPRS limits the accuracy that can be achieved
Positioning enhancement
  UTDOA support
  Positioning accuracy improvement
  Positioning power consumption reduction

## Slide 8: TDD enhancement for NB-IoT
In Rel-15 TDD NB-IoT, target is to support the same features as Rel-13 NB-IoT, additionally considering small-cells scenarios.However, Rel-14/Rel-15 NB-IoT has gone through considerable improvement.
TDD enhancement in Rel-16
  Early data transmission (EDT) support
  Wake-up signal support
  Multi-cast support
  HARQ feedback early termination

## Slide 9: Network maintenance enhancement for NB-IoT
SON functionality is supported for efficient network maintanence.
  Neighbor cell measurement report from UE for ANR(e.g. RSRP and/or RSRQ, and CGI provided).
  Neighbor cell status awareness for eNB power saving, self-configuration and self-healing.
UE differentiation enhancement for radio resource coordination.
  Maximal tolerable delay(e.g several hours or days for metering service) is provided per UE or per Service.
  UE or service based originating service prevention based on maximal tolerable delay is supported for NW congestion case.

## Slide 10: NB-IoT eNB connectivity to 5GC
Connectivity to 5G Core Network for the eNB supporting NB-IoT.
  Support 5G-CN functions. e.g.:
    Flow based QoS.
    New security scheme (if any).
  Simultaneous support for UEs connected to EPC and UEs connected to 5G-CN in the same cell.
  Enhancements for core network node selection functions, e.g. assist to perform initial NAS selection and NAS routing

## Slide 11: Thank you