## Slide 1: Views on REL-16 IoT

## Slide 2: REL-15 maintenance and REL-16 start
It will be declared in RAN#80 that REL-15 LTE MTC/NB-IOT work is completed. However, we observed that maintenance of REL-15 MTC/NB-IOT work still remains at least in RAN2.
During Q3/2018, at least RAN2 should further consolidate specification of very late inputs from RAN1#93 in Busan.
  RAN1 inputs to fresh agreements on introduction of BSR SPS and Dedicated SR came late in the evening on the 4th day of RAN2#102
RAN1 may start REL-16 LTE IoT right after June, while RAN2 should start it after September considering REL-15 maintenance work in RAN2.

## Slide 3: REL-16 scope for LTE IoT
RAN should focus on some essential enhancements that have been discussed during Rel-15 but was not introduced due to tight REL-15 schedule:
  Enhancements especially essential for TDD:
    cross-carrier operation(NB-IoT), DCI overhead reduction, HARQ feedback overhead reduction, early data termination (NB-IoT)
  Co-existence with NR
  Semi-Persistent Scheduling
  Mobile Terminating Early Data Transmission

## Slide 4: Single/multi-hop relay for REL-16 LTE IoT
Single/multi-hop relay for IoT devices is essential for deeper coverage support and network overhead reduction, to support practical market needs.
Compared to the traditional relay for legacy LTE UEs, the following aspects may have significant impacts and so require lots of TUs for IoT relay
  support of narrow band
  support of enhanced coverage
  support of low complexity devices
  support of low power consumption
To inquire and set appropriate target scenarios and requirements, reasonable study phase is necessary before starting specification works
The outcome of FeD2D study based on UE type relay can be considered as input to this work to speed up the work on relay.