## Slide 1: ZTE's view on Rel16 SIs and WIs
ZTE Corporation
June 1, 2018
RP-180786

## Slide 2: 3GPP R16 timeline
2nd Package approval

## Slide 3: Overall view
1st R16 package approval in June for new proposals
  Only WIs/SIs to be immediately started after June will be approved
  TUs for on-going SIs (i.e. NOMA,NR-U and IAB) in 2018 H2 should be considered together
  Leave one pool of TUs for potential WIs (as continuation of these 3 on-going SIs) in 2019
  Continue email discussions on other new proposals on RAN draft reflector
2nd R16 package approval in Dec.
  To approve WIs for NOMA, NR-U and IAB, based on the conclusion of corresponding SIs
  To approve additional NR SIs/WIs, if TUs are available (depending on level of interest, etc.)
Other SIs/WIs proposal not covered by 1st and 2nd package could be considered if consensus is achieved among companies

## Slide 4: NR track - 1st package (in June)
Not supportive:
  Spectrum efficiency enhancement (WI)
  Flexible duplex (SI)
  NR Broadcast (SI)
  NR-Voice (SI)
  Low layer CU-DU split (WI)
RAN1 leading:
  NR-URLLC (SI)
  NR-MIMO (WI)
  NR-V2X (SI)
  NR power consumption (SI)
  Remote interference management (SI)
  Non Terrestrial Network (SI)
RAN2 leading:
  No new WI or SI will be approved
RAN3 leading:
  SON/MDT (SI)

## Slide 5: NR track - 2nd package (to be approved in December)
RAN1 leading:
  NOMA (WI)
  NR-U (WI)
  NR-URLLC (WID)
  Power consumption (WID)
  Remote interference management (WID)
  Positioning (SI)
  Coverage enhancement (SI)
RAN2 leading
  IAB (WI)
  NR_IoT (SI)
  NR Mobility enhancement (WI)

## Slide 6: LTE track
NB-IoT and eMTC further enhancements
Enhancement for FWA and Stationary UE
  The gap is not so clear
HRLLC
  Rel15 LTE can meet ITU-R requirement and more stringent requirement can be met by NR
LTE Drones
  To introduce drone feature in NR is more important
Further mobility enhancement
  R15 LTE can already meet ITU-R requirement and seems not necessary to do it LTE track again
LTE high speed (up to 500km/h): no strong opinion
LTE MIMO: not necessary

## Slide 7: Detailed view on RAN1-led NR topics in 1st package
NR-URLLC
NR-V2X
NR-MIMO
NR-Power Consumption
NR-Remote Interference Management

## Slide 8: NR-URLLC
Basic channel enhancement
  Including UL/DL, control and data channel
  No new MCS/CQI design is necessary
  Focus on FR1
Address mixing eMBB and URLLC case
  Including UL/DL, intra/inter UE prioritization/multiplexing
  Multiple active BWP could be also considered
TSN enabler
  To address specific TSN service including timing, jitter, traffic model, etc.

## Slide 9: NR-V2X
Functionality
  NR-V2X should address both basic safety functionality and advanced use cases. It doesn’t necessarily mean NR-V2X will replace LTE V2X.
Objects:
  Both side link and Uu interface should be studied
  Including Uu based V2X scheduling
  RAT selection assuming non co-channel co-existence between LTE V2X and NR V2X
  Focus on frequency bands lower than 10GHz, e.g. 5.9GHz
Timeline:
  12 months study
  Based on conclusion of SID, RAN can discuss the necessity, duration and scope of potential WID

## Slide 10: NR-MIMO
Left-over items from Rel-15 should have highest priority
  Single DCI based multi-TRP/Panel operation, e.g., multiple DMRSCSI-RS QCL groups
  Aperiodic beam reporting with multiple resource sets
  PUCCH based BFR
Items well studied with attractive gains should be (potentially) specified
  Type II CSI enhancements: overhead reduction, extension to L>4, rank>2
  Reciprocity based CSI
  DCI/CSI enhancements for multi-TRP/Panel
  UL frequency selective precoding
  Group based/interference-aware beam management
Items requiring further study should be postponed to later release(s)
  Explicit feedback, non-linear precoding
  Non-transparent TxD
  Further enhancement on UL multi-panel
  Further enhancement on UL beam management

## Slide 11: NR-Power Consumption
Scenario:
  Prefer dense urban for both FR1 and FR2 with eMBB traffic model
Enhancement in RRC_CONNECTED only:
  Dynamic BWP adaption
  Reduced PDCCH monitoring
  Cross-slot scheduling
  Other potential enhancements should consider power saving gain and network performance

## Slide 12: NR-Remote Interference Management
Study mechanisms for improving network robustness and addressing strong remote base station interference [RAN1]
Study mechanisms for remote interference identification over the air interface, to allow identifying which gNB(s) generate strong remote interference, including the following aspects
  Reference signal design for gNB to identify that it creates strong inter-gNB interference to some victim gNB [RAN1]
  Mechanism for gNB to start and terminate the transmission/detection of the reference signal(s) [RAN1, RAN3]
Coordination among gNBs for mitigating remote interference, e.g., transmission power, beam, etc. [RAN3]

## Slide 13: Thank you