## Slide 1: Motivation for new WID on NR Support for Aerial Vehicles
Ericsson
RAN #80, La Jolla, CA, US, June 11 - 14, 2018
AI 9.2.2
RP-181071

## Slide 2: Preceding WI (RP-172826) (LTE)
In RAN#78, a WI on “Enhanced LTE Support for Aerial Vehicles” was approved in RP-172826.
This WI specified features that can improve the efficiency and robustness of terrestrial LTE network for delivering connectivity solutions more efficiently for UAVs.
These specified features include the following:
  subscription based identification
  height and location reporting based on triggering on height threshold
  interference detection based on measurement report triggering on an event where multiple cells’ RSRPs are above a threshold,
  flight path plan information via RRC from UE to eNB
  open loop power control enhancements were specified to mitigate UL interference on PUSCH.

## Slide 3: New WID on NR Support for Aerial Vehicles
The WID on ‘NR for Aerial Vehicles’ aims to specify the following improvements for NR support for aerial vehicles.
The objective is to specify the following improvements:
  Subscription based identification
  Height/location/airborne status based reporting
  Controlling the number of measurement reporting
Since the amount of commercial drones are expected to grow, we believe that it is crucial that NR supports drones at an early release.

## Slide 4: Subscription based identification
There is a clear need to identify drones in the network due to increased UL/DL interference and regional regulations concerning UAVs.
Signaling support of subscription based identification [RAN2 and RAN3]
  Specify signaling on NAS level to support subscription based aerial UE identification

## Slide 5: Height/location/airborne status reporting
In order to assist the network support for drones, the reporting of height, location and airborne status is very beneficial in order for the network to apply correct configurations.
Specify enhancements to report height, location or airborne status to assist network [RAN2].

## Slide 6: Controlling the number of measurement reporting
In TR 36.777, it was shown that the amount of measurement reporting was greatly increased for aerial UEs in LTE networks.
As the reporting may be triggered per beam in NR, the amount measurement reporting is expected to be more severe.
Specify enhancements to reduce the amount of measurement reporting [RAN2]