## Slide 1
3GPP TSG RAN Meeting #80 RP-181129
La Jolla, USA, June 11 - 14, 2018
Agenda Item: 9.2.4
Source: Keysight Technologies
Title: Motivation for continued development of OTA requirements and test methods
Document for: Information
Motivation for continued development of OTA requirements and test methods

## Slide 2: The problem – basic antenna efficiency has been getting worse for years
1990
1995
2000
2005
2010
2015
0 dBi
-10 dBi
-20 dBi
Illustrative isotropic antenna performance
Free space
Head/hand loss

## Slide 3: The cause
Integration of antennas
Reducing volume for antennas
Introduction of MIMO
Multi-band support
Carrier aggregation

## Slide 4: Conducted vs. OTA
The cabled environment has no dimensions. By comparison there are many OTA environments n which we could specify and test requirements
 | Conducted | OTA
Speed of specifying requirements | Fast | Historically very slow
Measurement uncertainty | < 1 dB | 2 dB to 6 dB
Test time | Fast | Slow due to 3D aspects
Connectivity cost | Low (cables) | High (shielded chambers)
Predictor of end-user performance | Increasingly unrealistic | Realistic
Ideal single signal LoS
Single signal LoS with non-spatial fading
Single signal with spatial fading
Single signal with dynamic spatial fading
Ideal dual signal LoS
Dual signal with non-spatial fading
Dual signal with spatial fading
Ideal dual signal dynamic LoS
Dual signal with dynamic non-spatial fading
Dual signal with dynamic spatial fading
Single signal with beamsweeping and spatial fading
Ideal multiple signal single direction LoS

## Slide 5: The 3GPP OTA Response for 3G and 4G
UMTS - SISO OTA requirements (TRP/TRS) introduced
  Took 3 years to agree requirements
LTE - No SISO OTA requirements agreed
  Work started in 2012 and stopped in 2017
  Too much time elapsed and UE performance was too wide to agree limits
LTE – Basic MIMO OTA requirements agreed
  Took 8.5 years to agree first testable requirements
  Most of the time was agreeing test environment and method

## Slide 6: The consequence
At < 6 GHz, extensive radio testing at the temporary antenna connector provides no indication of how UEs will perform in the field
Lack of LTE SISO OTA requirements means network performance is unknown
Bilateral operator/vendor agreement may apply in some cases
Existence of only basic open loop TM3 MIMO OTA requirements means the radiated performance and value of many LTE features introduced since Release 8 is unknown
  Higher order MIMO, CA, interference cancellation, other transmission modes

## Slide 7: The 3GPP OTA Response so far for 5G NR
The first NR specifications for Rel-15 have been delivered in June 2018
However, compressed timescales mean current completeness of NR is significantly less than for LTE in Release 8 in Dec 2008
NR FR1 - No OTA requirements in Rel-15
NR FR2 – Basic OTA requirements introduced
  Peak EIRP and spherical coverage
  OTA demodulation scope limited to “wireless cable” RF/baseband (excludes antenna)
  No spatial RRM requirements

## Slide 8: Specification completeness LTE vs NR
Page count* | LTE Rel-8 Dec 2008 | LTE Rel-8 Sep 2017 | LTE Rel-14 Sep 2017 | NR FR2 Rel-15 Dec 2017
Physical layer | 80 | 81 | 190 | 73
UE Radio core | 26 | 34 | 353 | 18
UE Radio performance | 11 | 42 | 739 | 0
Total (Radio part) | 147 | 388 | 3588 | 33
RRM Page count* | LTE Rel-8 Dec 2008 36.133 v8.4.0 | LTE Rel-8 Sep 2017 36.133 v8.23.0 | LTE Rel-14 Mar 2018 36.133 v14.7.0 | NR SA Rel-15 Dec 2017 TS 38.133 v15.0.0 | NR SA Rel-15 Mar 2018 TS 38.133 v15.1.0
UE RRM core | 60 | 64 | 559 | 30 | 47
UE RRM performance | 50 | 248 | 2260 | 0 | 0
Total (RRM part) | 110 | 312 | 2819 | 30 | 47
* Excluding non-technical pages -TOC, change history etc.
* Excluding non-technical pages -TOC, change history etc.
The physical layer specifications appear to be in good shape, sufficient to design devices, but many core radio and RRM requirements were down-scoped to meet the Dec 2017 deadline.

## Slide 9: The OTA opportunity for 5G NR @ FR1
LTE set a bad OTA precedent given that the pressure on antenna design got higher but no requirements were agreed
For NR @ FR1 the first priority should be for the new bands n77, n78 and n79 (3.3 to 65 GHz) that SISO requirements are agreed early to prevent a repeat of what happened in LTE
The extension of SISO requirements to the other “n” FR1 bands
Applying any NR resulting requirements to LTE from Rel-16 should be considered

## Slide 10: The OTA opportunity for 5G NR @ FR1 Moving to a closed loop metric
The existing LTE metric Total Radiated Multi-antenna Sensitivity (TRMS) is slow to measure and is not representative of normal closed loop network operation
MCS n + 6
MCS n + 5
MCS n + 4
MCS n + 3
MCS n + 2
MCS n + 1
MCS n
Power or SIR
Throughput
Closed loop performance using variable MCS and rank (target BLER 90 % of MCS)
Open loop TRMS performance using fixed RMC and forced rank 2
  Closed loop benefits
  Tests UEs in a way that much better matches real network operation
  Approximately 10x faster than TRMS
  Different SIRs can be used for different deployment scenarios
  The principles of closed loop testing are already defined in TR 37.901 and is a simple change to existing test method
  Will show if a UE’s best performance is rank 1 or 2

## Slide 11: The OTA opportunity for 5G @ FR1 Evolution of existing test methods
Feature | MPAC | RTS
Higher frequency | Test zone is 0.85 λ for an 8x2 configuration (10 cm @ 2.6 GHz, 5 cm @ 5 GHz). 16x2 would provide ~2 λ or 12 cm @ 5 GHz – enough for some smartphones. Then move to 24 x 2 for larger devices or antenna declaration | No impact on test zone size for a typical SISO chamber
Higher order MIMO | Can inherently handle any order of MIMO, however, each doubling of the order requires double the channel emulator resources which are already high | RTS will scale to 4x4 using two cross polarized probes but 8x8 unlikely due to isolation of the 8 wireless cable streams
Carrier Aggregation | Can inherently handle an level of CA but same issue as for higher order MIMO – CE hardware | RTS scales well for CA as the doubling and tripling of CE resources is starting from a much lower base
Advanced interference emulation | Addition of more sophisticated interference is possible but requires more CE hardware | Similar to MPAC but from a lower base
Increased active antenna usage | MPAC has no issues with active antennas or dynamic antenna switching during the test sequence | RTS can only test a static antenna configuration and would require a UE beamlock function as agreed for FR2 to ensure a static configuration

## Slide 12: The OTA opportunity for 5G @ FR2 Demod
Basic line of sight RF requirements are being developed
This leaves demod and RRM as the prime new areas
For demod @ FR2, the challenges are different to LTE FR1
  The channel perceived by the UE will be much more sparse due to gNB Tx spatial filtering (8x8 array., 12 degree HPBW)
  The Rel-15 scope is MIMO rank 2 with cross polarized transmission
The consequence is that it is not the shape or pattern of the UE antenna that influences performance but its direction
Only when rank 4 is considered which requires two independent directions will the shape of the antennas matter as in FR1
The extent to which the UE antenna pattern influences 2x2 cross-polarized MIMO performance needs to be studied to determine if the current plan for non-spatial “wireless cable” OTA requirements is sufficient

## Slide 13: The OTA opportunity for 5G @ FR2 RRM - initial access
It is in the area of RRM @ FR2 where the biggest challenge lies for NR
At FR1 all RRM requirements were non-spatial and based on the frequency, power level and timing of multi-cell test signals
At FR2, space needs to be added to that list
The most critical new spatial RRM requirement will be for initial access where up to 64 Tx directions can be used for the SSB which are further modified by the channel model
Defining a test method for this will be difficult but extremely important if initial access is to be controlled
SS Block 1
SS Block 2
SS Block 3
SS Block 4
SS Block 5

## Slide 14: The OTA opportunity for 5G @ FR2 RRM – beam refinement
Following on from initial access will be the need to define requirements for beam refinement so the link can be maintained in connected mode
This will include the need to spatially monitor adjacent cells and define handover criteria where space is the critical domain – not just signal level as was the case @ FR1
Performance requirements in this area need to include sufficient random elements to ensure UE’s are not designed to pass a narrow set of predictable scenarios
In addition to the spatial evolution of the network due to travel – which will be significant given the expected smaller geometries – the UE’s orientation towards the network is also an important variable
Test environments for beam refinement will need far fewer directions than for initial access but the AoA will need to evolve based on travel

## Slide 15: Summary
The need for OTA requirements and validation has been steadily growing since the early days of 3G
The 3GPP OTA requirements have not kept up with the growing sophistication of the air interface, which increasingly relies on exploiting the spatial domain
At FR1, the opportunity is to specify requirements that demonstrate the OTA performance and value of the many new features introduced since |release 8
At FR2 the big new issue is the spatial domain
Signals will have very narrow beamwidth, and spatial dynamics due to movement in the network will make establishing and maintaining a reliable link much harder than was ever the case @ FR1
For FR2 mobile communications to be reliable, this new spatial environment needs to be sufficiently specified and tested or the result will be poor user experience
Support for the SID in [1] is requested
Further reading can be found in the references [2] – [4]

## Slide 16: References
[1] RP-181026 “New SID on Study on radiated test methodology for the verification of multi-antenna reception performance of NR Ues”
[2] IEEE ComSoc Making 5G Work – Capacity Growth and RF Aspects
[3] IEEE ComSoc Making 5G Work – Data Throughput and Radio Resource management
[4] COST IRACON IC1504 TD(18)07051 Next steps in channel modelling and OTA test methods for 5G