## Slide 1: Change of carrier frequency lower boundary supporting maximum 8 SS/PBCH blocks
3GPP TSG RAN Meeting #81 RP-181833
Gold Coast, Australia, Sept 10 - 13, 2018
Source: CMCC
Title: Change of carrier frequency lower boundary supporting maximum 8 SS/PBCH blocks
Document for: Discussion
Agenda Item: 9.2.1

## Slide 2: Background
The number of supported number of SS/PBCH blocks and pattern for FR1 is defined in current spec TS 38.213 as following
  For a half frame with SS/PBCH blocks, the first symbol indexes for candidate SS/PBCH blocks are determined according to the subcarrier spacing of SS/PBCH blocks as follows, where index 0 corresponds to the first symbol of the first slot in a half-frame.
  - Case A - 15 kHz subcarrier spacing: the first symbols of the candidate SS/PBCH blocks have indexes of {2, 8} + 14*n. For carrier frequencies smaller than or equal to 3 GHz, n=0, 1. For carrier frequencies larger than 3 GHz and smaller than or equal to 6 GHz, n=0, 1, 2, 3.
  - Case B - 30 kHz subcarrier spacing: the first symbols of the candidate SS/PBCH blocks have indexes {4, 8, 16, 20} + 28*n. For carrier frequencies smaller than or equal to 3 GHz, n=0. For carrier frequencies larger than 3 GHz and smaller than or equal to 6 GHz, n=0, 1.
  - Case C - 30 kHz subcarrier spacing: the first symbols of the candidate SS/PBCH blocks have indexes {2, 8} + 14*n. For carrier frequencies smaller than or equal to 3 GHz, n=0, 1. For carrier frequencies larger than 3 GHz and smaller than or equal to 6 GHz, n=0, 1, 2, 3.
It can be observed that only for carrier frequencies larger than 3 GHz in FR1, maximum of 8 SS/PBCH blocks is supported.
Although n41 is a strong candidate for the first phase of NR deployment, according to current spec, only at most 4 SS/PBCH blocks can be supported

## Slide 3: Background-Frequency definition in TS38.101-1
NR operating band | Uplink (UL) operating band BS receive / UE transmit FUL_low – FUL_high | Downlink (DL) operating band BS transmit / UE receive FDL_low – FDL_high | Duplex Mode
n1 | 1920 MHz – 1980 MHz | 2110 MHz – 2170 MHz | FDD
n2 | 1850 MHz – 1910 MHz | 1930 MHz – 1990 MHz | FDD
n3 | 1710 MHz – 1785 MHz | 1805 MHz – 1880 MHz | FDD
n5 | 824 MHz – 849 MHz | 869 MHz – 894 MHz | FDD
n7 | 2500 MHz – 2570 MHz | 2620 MHz – 2690 MHz | FDD
n8 | 880 MHz – 915 MHz | 925 MHz – 960 MHz | FDD
n12 | 699 MHz – 716 MHz | 729 MHz – 746 MHz | FDD
n20 | 832 MHz – 862 MHz | 791 MHz – 821 MHz | FDD
n25 | 1850 MHz – 1915 MHz | 1930 MHz – 1995 MHz | FDD
n28 | 703 MHz – 748 MHz | 758 MHz – 803 MHz | FDD
n34 | 2010 MHz – 2025 MHz | 2010 MHz – 2025 MHz | TDD
n38 | 2570 MHz – 2620 MHz | 2570 MHz – 2620 MHz | TDD
n39 | 1880 MHz – 1920 MHz | 1880 MHz – 1920 MHz | TDD
n40 | 2300 MHz – 2400 MHz | 2300 MHz – 2400 MHz | TDD
n41 | 2496 MHz – 2690 MHz | 2496 MHz – 2690 MHz | TDD
n51 | 1427 MHz – 1432 MHz | 1427 MHz – 1432 MHz | TDD
n66 | 1710 MHz – 1780 MHz | 2110 MHz – 2200 MHz | FDD
n70 | 1695 MHz – 1710 MHz | 1995 MHz – 2020 MHz | FDD
n71 | 663 MHz – 698 MHz | 617 MHz – 652 MHz | FDD
n75 | N/A | 1432 MHz – 1517 MHz | SDL
n76 | N/A | 1427 MHz – 1432 MHz | SDL
n77 | 3300 MHz – 4200 MHz | 3300 MHz – 4200 MHz | TDD
n78 | 3300 MHz – 3800 MHz | 3300 MHz – 3800 MHz | TDD
n79 | 4400 MHz – 5000 MHz | 4400 MHz – 5000 MHz | TDD
n80 | 1710 MHz – 1785 MHz | N/A | SUL
n81 | 880 MHz – 915 MHz | N/A | SUL
n82 | 832 MHz – 862 MHz | N/A | SUL
n83 | 703 MHz – 748 MHz | N/A | SUL
n84 | 1920 MHz – 1980 MHz | N/A | SUL
n86 | 1710 MHz – 1780MHz | N/A | SUL

## Slide 4: Motivation
NR coverage is crucial for operators guarantee user experience by reusing existing infrastructure, if comparable or even better coverage than LTE can be achieved
Massive MIMO is important in improving coverage of 5G NR deployment, where the sweeping of broadcast channels and common control channels are an important feature to extend the network coverage
For n41, compared with massive MIMO capability with 3.5GHz, it can be implemented with the same number of antenna elements (e.g. 128 or 192 elements), number of TXRUs (e.g. 64 TXRUs) under comparable size and heat-dissipation capability, which means the massive MIMO implementation for 2.6GHz enable as similar narrow beam sweeping in both horizontal and vertical domain as that for above 3GHz carrier frequency
Furthermore, considering the total bandwidth of n41 (almost 200MHz wide), due to state-of-art of PA, the transmitting power maybe hard to increase linearly to cover this whole band with target power density in one RRU. Therefore, it is expected to allow supporting more SS/PBCH blocks in n41 to offer more flexibility to product implementation by taking PA status into account
However, current spec only allows maximum 4 SS/PBCH blocks for carrier frequencies smaller than 3GHz
Notes: 垂直维

## Slide 5: Observations and proposals
Observation 1: For carrier frequencies around 2.5GHz, there are both FDD (n7) and TDD (n38, n41) bands.
Proposal:
Proposal option 1: Change the carrier frequency lower boundary supporting maximum 8 SS/PBCH blocks to 2.4GHz without differentiating paired or unpaired spectrum
  This changes the supported maximum number of SS/PBCH blocks to 8 for both bands n7 and n38/41.
  For UE during initial access, this option is a bit simpler, since UE does not need to try two different interpretations for PBCH-DMRS. However, this requires SFN synchronization requirement among FDD gNBs to be within 2.5ms, since there is no half-radio frame indication in PBCH-DMRS.
Proposal option 2: Change the carrier frequency lower boundary supporting maximum 8 SS/PBCH blocks to 2.4GHz and limit it to unpaired spectrum only
  This option will not impose finer synchronization accuracy on the requirement for SFN synchronization in FDD, consequently, UE needs to try two hypothesis for PBCH descrambling.
Note: Proposal option 1/2 depends on balance between the expectation on coverage and the concern on maintaining a bit finer synchronization accuracy for FDD in band n7.

## Slide 6
Appendix

## Slide 7: Supported SSB pattern and SCS [TS38.101]
NR Operating Band | SS Block SCS | SS Block pattern1 | Range of GSCN (First – <Step size> – Last)
n7 | 15kHz | Case A | 6554 – <1> – 6718
n38 | 15kHz | Case A | 6431 – <1> – 6544
n41 | 15kHz | Case A | 6246 – <3> – 6714
 | 30 kHz | Case C | 6252 – <3> – 6714
NOTE 1: SS Block pattern is defined in section 4.1 in TS 38.213 [8] |  |  |