## Slide 1: Dynamic Power Sharing vs. Dynamic NR Dropping (Concerns about NR transmissions for EN-DC under power limited condition)
RP-181891
RAN#81, Gold Coast, Australia
10-13 September, 2018
Sprint, Deutsche Telekom

## Slide 2: What is EN-DC Dynamic Power Sharing?
Dynamic power sharing allows for UE uplink power to be efficiently allocated to LTE and/or NR as needed in EN-DC.
Dynamic power sharing capable UEs have the ability to adjust power so that maximum levels are not exceeded

## Slide 3: Dynamic Power Sharing with NR Scaling
UE: How many slices of pizza do you want?
LTE: 4
NR: 5
UE: Sorry, we don’t have enough. LTE can have 4 and NR can have 4
Currently this behavior is allowed for EN-DC, but not mandatory

## Slide 4: Dynamic Power Sharing with NR Dropping
UE: How many slices of pizza do you want?
LTE: 4
NR: 5
UE: Sorry, we don’t have enough. LTE can have 4 and NR gets zero.
Currently this behavior is apparently allowed for EN-DC
(Be careful which RAN1 delegates you agree to share a pizza with.  )

## Slide 5: What is the benefit of Dynamic NR Power Scaling over Dynamic NR Dropping?
The RF environment changes rapidly. Even when a UE thinks it doesn’t have enough power for the UL NR transmission to be successful, the power may actually be sufficient.
Through the use of Hybrid ARQ and soft decisions in the receiver, a base station can process UL transmissions together with retransmissions to increase gain and Forward Error Correction (FEC).
With standalone LTE and NR if a UE thinks that more power is needed than is available, it doesn’t just drop a transmission. EN-DC shouldn’t treat lack of power any differently.

## Slide 6: A second troubling issue with Dynamic NR dropping
LS R1-1715313 from RAN1 to RAN2 and RAN4 says:
Note: The network will still have flexibility to prioritize or reserve certain NR transmission power depending on network implementation
This LS on power sharing clearly says that the network will still have the ability prioritize or reserve certain NR transmission power. So, for a UE capable of PC3 (23 dBm) for inter-band EN-DC, the network might want to set P_LTE to 20 dBm and P_NR to 23 dBm, ensuring that at least 20 dBm is reserved for NR. However, if the UE is always allowed to drop NR for this configuration when power sharing is needed, then that takes away the network’s ability to reserve or prioritize certain NR transmission power.
This is another good reason that the decision to drop NR completely shouldn’t be left up to the UE.

## Slide 7: Potential Options for RAN Plenary
Do nothing. Have no differentiation between Dynamic Power Sharing with NR power scaling UEs and Dynamic NR Dropping UEs.
Allow complete dropping of NR only under bounded conditions to be determined by RAN4 (i.e. >X dB of scaling required, or if the LTE-NR PSD difference is more than Y dB with X and Y defined by RAN4)
  Approve CR in RP-181892 and then resolve any discrepancy in 38.213
Create a third category of UEs that requires dynamic power scaling so there would be:
  Type 0: Dynamic NR Power Scaling capable (complete NR dropping only allowed under bounded conditions to be determined by RAN4)
  Type 1: Dynamic Power Sharing capable (NR dropping allowed)
  Type 2: Not Dynamic Power Sharing capable

## Slide 8: Background and technical details

## Slide 9: Endorsed Draft CR for inter-band EN-DC PCMAX
R4-1811484 Pcmax for inter-band EN-DC FR1 draft CR 38.101-3 CR- rev Cat: F (Rel-15) v15.2.0 Source: InterDigital, Inc.
Abstract:
Pcmax for inter-band EN-DC FR1 draft CR.
Discussion:
Ericsson: we have technical concern on this CR and definition of the configured total output power. But if Ericsson is the only company against this CR, we accept this CR. [This should allow NR to drop if lower total output power exceeds]
Decision: The document was endorsed.

## Slide 10: Calculation of PCMAX_ EN-DC _L in 38.101-3
If 10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)] > MIN { PEMAX, EN-DC ,PPowerClass, EN-DC}
Then
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) ], PEMAX, EN-DC ,PPowerClass, EN-DC}
Else
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)], PEMAX, EN-DC ,PPowerClass, EN-DC}
where
pCMAX H _ E-UTRA,c (p) is the E-UTRA higher limit of the maximum configured power expressed in linear scale;
pCMAX H _ NR,c (q) is the NR higher limit of the maximum configured power expressed in linear scale;
pCMAX L _ E-UTRA,c (p) is the E-UTRA lower limit of the maximum configured power expressed in linear scale;
pCMAX L _ NR,c(q) is the NR lower limit of the maximum configured power expressed in linear scale;
PPowerClass, EN-DC is defined in sub-clause 6.2B.1.3-1 for inter-band EN-DC;
PEMAX, EN-DC is PMAX, EN-DC value signaled by RRC and defined in [7];

## Slide 11: What is PCMAX (In layman’s terms)
Pcmax is the value that a UE uses for configured maximum output power.
A UE is allowed to reduce its maximum transmit power below the UE power class and p-Max limits in order to meet emissions requirements
RAN4 has specifications for Maximum Power Reduction (MPR) and Additional Maximum Power Reduction (A-MPR)
RAN4 specifies a range of PCMAX_H and PCMAX_L that PCMAX can be configured between, where the lower value reflects maximum MPR/A-MPR.
Under test, a UE is told to increase its power using the TPC UP command to ensure that reaches PCMAX and it does not take more back-off than necessary to meet emissions requirements.

## Slide 12: Pcmax for interband EN-DC for Type 1 UEs
For EN-DC there is Pcmax_LTE, Pcmax_NR and Pcmax_EN-DC, each of which has a range
Type 1 (dynamic power sharing capable) UEs are supposed to be able to handle power sharing between LTE and NR.
This feature is named “Dynamic Power Sharing,” and not “Dynamic NR Dropping”

## Slide 13: Example of a troubling scenario
PEMAX,EN-DC = PPowerClass,EN-DC = 23 dBm
PCMAX L _ E-UTRA,c (p) = 20 dBm
PCMAX L _ NR,c (q) = 21 dBm
10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,NR,c(q)] > MIN { PEMAX, EN-DC ,PPowerClass, EN-DC}
  so PCMAX_ EN-DC _L(p,q) = PCMAX L _ E-UTRA,c (p) = 20 dBm
In this scenario, there is enough power left over that NR could be transmitted at 20 dBm and still have the UE output power be within the 23 dBm limit required by PEMAX,EN-DC = PPowerClass,EN-DC = 23 dBm.
However, since PCMAX_ EN-DC _L(p,q) is set to 20 dBm, instead of reducing power by 1 dB and transmitting at 20 dBm, the UE is allowed to unilaterally decide to lower the NR power all the way to nothing (drop NR) for no good reason, other than a strict interpretation of TS 38.213 seems to allow it.
MPR and/or A-MPR for NR would be untestable in this scenario, since NR is allowed to be completely dropped regardless of MPR or A-MPR.

## Slide 14: A better approach? A simpler equation for PCMAX_EN-DC
If 10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)] > MIN { PEMAX, EN-DC ,PPowerClass, EN-DC}
Then
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) ], PEMAX, EN-DC ,PPowerClass, EN-DC}
Else
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX_L_NR,c (q)], PEMAX, EN-DC ,PPowerClass, EN-DC}
If 10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)] > MIN { PEMAX, EN-DC ,PPowerClass, EN-DC} then LTE keeps the pCMAX L _ E-UTRA,c (p) and NR power is scaled down (may be dropped when below TBD threshold)
where
pCMAX H _ E-UTRA,c (p) is the E-UTRA higher limit of the maximum configured power expressed in linear scale;
pCMAX H _ NR,c (q) is the NR higher limit of the maximum configured power expressed in linear scale;
pCMAX L _ E-UTRA,c (p) is the E-UTRA lower limit of the maximum configured power expressed in linear scale;
pCMAX L _ NR,c(q) is the NR lower limit of the maximum configured power expressed in linear scale;
PPowerClass, EN-DC is defined in sub-clause 6.2B.1.3-1 for inter-band EN-DC;
PEMAX, EN-DC is PMAX, EN-DC value signaled by RRC and defined in [7];

## Slide 15: Advantage of this approach?
The UE would not be able to make an arbitrary decision on when to completely drop NR
The NR UL transmissions can be combined via HARQ so that UL resources aren’t wasted
MPR and A-MPR for EN-DC would be testable, even when
10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,NR,c(q)] > MIN { PEMAX, EN-DC ,PPowerClass, EN-DC}
  NR MPR/A-MPR could be exceeded only when necessary.

## Slide 16: Downside of this approach?
A slight discrepancy between RAN4 and RAN1, where NR could only be completely dropped when it would be below a threshold to be defined by RAN4.
One possible resolution would be to change one symbol in TS 38.213 from “” to “=“ and added note as follows:
  if MCG(i1)+SCG(i2) > in any portion of slot i2 of the SCG, the UE reduces transmission power in any portion of slot i2 of the SCG so that MCG(i1)+ SCG(i2) in any portion of slot i2 , where MCG(i1) and SCG(i2) are the linear values of the total UE transmission powers in subframe i1 of the MCG and in slot i2 of the SCG, respectively.
Changed to:
  if MCG(i1)+SCG(i2) > in any portion of slot i2 of the SCG, the UE reduces transmission power in any portion of slot i2 of the SCG so that MCG(i1)+ SCG(i2) in any portion of slot i2 , where MCG(i1) and SCG(i2) are the linear values of the total UE transmission powers in subframe i1 of the MCG and in slot i2 of the SCG, respectively. Note: for partial overlap between LTE and NR, MCG(i1)+SCG(i2) may be below