## Slide 1
3GPP TSG RAN Meeting #82
Sorrento, Italy, December 10-13, 2018
Agenda Item: 9.1.2
RP-182323
Motivation for WI on
Integrated Access and Backhaul for NR
Qualcomm Inc.

## Slide 2: IAB Study Item
SI approval: In RAN #75, SI for Integrated Access and Backhaul for NR was approved in RP-170831
SI goal: Support for wireless backhauling to enable flexible and very dense deployment of NR cells without the need for densifying the transport network
SI objectives:
  Efficient and flexible operation for both in-band and out-of-band scenarios
  Multi-hop and redundant connectivity
  End-to-end route selection and optimization
  Support of backhaul links with high spectral efficiency
  Support of legacy NR UEs
  Topology management for single-hop/multi-hop and redundant connectivity
  Route selection and optimization
  Dynamic resource allocation between the backhaul and access links
  High spectral efficiency while also supporting reliable transmission
SI completion: According to schedule with very narrow recommendations for work item.

## Slide 3: IAB Work Item: Justification
IAB needed to enable flexible and dense deployment of NR cells without densifying transport network.
Short range of mmWave access creates need for densified deployment with multi-hop backhauling.
Larger bandwidth available for NR (e.g. mmWave spectrum) provides opportunity for self-backhauling.
In-band access and backhauling allow tight interworking and resource-efficient accommodation of half-duplex constraint.
Multi-beam systems and MIMO reduce cross-link interference allowing higher densification.
Short-term blocking of mmWave backhaul links demands fast switching of access and backhaul links.

## Slide 4: IAB Work Item: Main objectives for RAN-3
WI objectives closely follow recommendation by IAB SI
  IAB leverages NR CU/DU split architecture
    IAB-node holds NR DU and MT functionality
  Centralized management at CU for topology- and route adaptation as well as resource allocation.
  Functionality to support IAB-node operation in NSA and SA mode
  Support of IP routability to IAB-node from wireline fronthaul enables reuse of native F1.

## Slide 5: IAB Work Item: Main objectives for RAN-2
WI objectives closely follow recommendation by IAB SI
  New “Adaption layer” above RLC enables routing across multi-hop topology
  Aggregation of UE DRBs to BH-RLC-channels supports scalability to many UEs
  Extension of LCID-space and signalling enhancements support fine-granular QoS for individual UE-bearers across multi-hop BH.
  Hop-by-hop signalling support enables low latency scheduling, BH RLF handling and dynamic resource coordination.
  Flow-control and hop-based RLC ARQ enable reliable transport across multiple hops.
N:1 and 1:1 bearer mapping

## Slide 6: IAB Work Item: Main objectives for RAN-1/4
WI objectives closely follow recommendation by IAB SI
  Heavy reuse of NR PHY specifications for backhaul link.
  Node integration reuses SSB/RMSI periodicity from NR access.
  Inter-IAB-node discovery independent of access via TDMed/FDMed SSBs/RMSI
    Muting pattern to address half-duplexing for inter-node discovery.
  Efficient resource utilization through semi-static and dynamic TDM among BH- and access-links
    New IAB-node DU resource types: DL hard/soft, UL hard/soft, Flexible hard/soft, Not available
    Dynamic indication of resources availability to downstream child node
  Synchronous operation through OTA signaling supporting e.g. indoor deployments
    Potential need to define timing requirements for IAB-specific network synchronization
  Potentially new requirements for RF co-existence of access and backhaul