## Slide 1: Data forwarding for Inter-system HO
NTT DOCOMO, INC., Vodafone, Telstra, Deutsche Telekom, Ericsson, Fujitsu
RP-182735
Revision of R2-182456
3GPP TSG-RAN Meeting #82
Sorrento, Italy, 10th - 13th December 2018

## Slide 2: Background
Data forwarding on Inter-system HO is discussed for a long time.
However, there were still two solutions in RAN3#102.(i.e. solution 2 and solution 3)
In the meeting, working agreement was made to adopt Option 2.
Option 2 does not allow direct data forwarding, which is requested by co-signing companies
This paper illustrates the outline and difference of these options and propose way forward to achieve direct data forwarding.

## Slide 3
Adding QFI to data and end marker, muxing into one tunnel
Behaves as in intra-system HO towards a target NG-RAN node
Behaves as in intra-system towards a source eNB
Transparent
Removing QFI from data and end marker, de-muxing into E-RAB tunnels

## Slide 4
Adding QFI to data and end marker, muxing into one tunnel
Behaves as in intra-system HO towards a source NG-RAN node
Behaves as in intra-system HO towards a target eNB
Transparent (indirect) or not in forwarding path (direct)

## Slide 5: Comparison of Options
No huge difference except that only Option 3 can achieve direct data forwarding.
  Furthermore, RAN3 already support both options from interface point of view (i.e. necessary IEs are already there for intra-system HO).
 | Option 2 | Option 3 | Note
Functional Impact | -More on UPF -Less on NG-RAN | -None on UPF -None in NG-RAN | Option 3 re-uses functions from intra-system HO
Interface impact | Already supported (for intra-system HO) |  | -Necessary IEs are already there for intra-system HO (“Clarification” is not considered as impact in this part.)
Freedom of configuration | Require coordination between source and target RAN node |  | Otherwise, data forwarding is impossible.
Direct data forwarding | Impossible | Possible (if direct transport is available.) | 

## Slide 6: Summary and way forward
Option 2 should be admitted as indirect data forwarding based on RAN3 working agreement.
However, only Option 3 enables direct data forwarding.
Furthermore, Option 3 doesn’t require interface impact. (i.e. necessary IEs are already there for intra-system HO).
Thus, following is proposed as WF (as package).
  Apply Option 2 for indirect data forwarding (based on working agreement)
  Apply Option 3 for direct data forwarding (additionally)