## Slide 1: WF on Beam Correspondence
Samsung
RP-182853
3GPP TSG RAN meeting #82
Sorrento, Italia, December 10 – 13, 2018

## Slide 2: Introduction
Conclusion about RP-182780 was as follows:
  Pages 2 and 3 were agreed
  Regarding page 4, it was agreed to define one tolerance level for the beam correspondence tolerance requirement
Regarding the signaling support for the beam correspondence requirement, it is proposed to select Alt2 of RP-182780, i.e.,
  Redefine the meaning of the existing UE feature 2-20 capability signaling
    UE that meets the requirement without the uplink beam sweeping should set the bit to 1
    UE that meets the requirement with the uplink beam sweeping should set the bit to 0
In addition, the followings are proposed:
  Beam correspondence (UE feature 2-20) is applicable only for FR2
  Uplink beam management (UE feature 2-30) is UE optional with capability signaling
    UE feature 2-30 should be set to 1 if UE feature 2-20 is set to 0
The following slides implement the above and also implement editorial fixes
  Changes w.r.t. pages 2 and 3 of RP-182780 are shown with revision marks

## Slide 3: Proposal
Clarify in TS 38.306 that beam correspondence (UE feature 2-20) is applicable only for FR2
Beam correspondence (UE feature 2-20) is UE mandatory with capability signaling
  UE that fulfills the beam correspondence requirement without the uplink beam sweeping should set the bit to 1
  UE that fulfills the beam correspondence requirement with the uplink beam sweeping should set the bit to 0
Uplink beam management (UE feature 2-30) is UE optional with capability signaling
  UE feature 2-30 should be set to 1 if UE feature 2-20 is set to 0
RAN4 to define details of the beam correspondence tolerance requirements given in the next slide which needs to be decided in RAN#82
Remove the contents of section 6.6.4 of the big CR to 38.101-2 in RP-182359
No change on the existing RAN4 agreement on minimum peak EIRP and spherical coverage requirements in TS 38.101-2 section 6.2.1.3
RAN4 to revise the test procedure for minimum peak EIRP and spherical coverage requirements so that the UE may rely on uplink beam sweeping during the test based on OEM declaration among the followings:
  Using the downlink reference signals only
  Using the downlink reference signals and uplink beam sweeping
Beam correspondence requirement is considered to be fulfilled if
  the UE meets the minimum peak EIRP and spherical coverage requirements without the uplink beam sweeping and meets the beam correspondence tolerance requirements; or
  the UE meets the minimum peak EIRP and spherical coverage requirements with the uplink beam sweeping and meets the beam correspondence tolerance requirements
The UE that passes minimum peak EIRP and spherical coverage requirements without the uplink beam sweeping does not need to be tested against the BC tolerance requirement in the next slide

## Slide 4: Beam correspondence tolerance requirements
RAN4 should specify the procedure and a single tolerance level requirement for beam correspondence by RAN#84 as follows
  For each of the test points in the grid, two EIRP should be calculated.
    EIRP1 is calculated based on the beam the UE chooses autonomously (corresponding beam) to transmit in the direction of the incoming DL signal. Procedure is based on what is described in section 5.2.1.3.7 of TR38.810 (R4-1816258)
    EIRP2 is the best EIRP (beam yielding highest EIRP in a given direction) which is based on UL beam sweeping or TE scan
      RAN4 should specify the procedure how the best EIRP is defined and derived
    Delta EIRP = EIRP2-EIRP1
    The test grid points where beam correspondence is verified are the grid points where the UE meets the spherical coverage requirements as specified in 6.2.1.3 of TS38.101-2
  The Delta EIRP CDF is obtained from the Cumulative Distribution Function (CDF) computed using Delta EIRP from all test points.
    For power class 3 UEs which support beam correspondence in single FR2 band, the requirement is fulfilled if the UE’s corresponding UL beams satisfy the following conditions
      [X]-percentile of delta EIRP CDF is no more than [Y] dB
    RAN4 to choose X between 80 and 100 by RAN#83
    RAN4 to choose Y by RAN#84
  The presence of both SSB and CSI-RS signals is assumed and Type D QCL is maintained between SSB and CSI-RS.
    The presence of both SSB and CSI-RS signals is defined in either RAN4 or RAN5 specs.