## Slide 1: Motivation for new WID: NR V2X
Source: LG Electronics
Document for: Discussion
Agenda Item: 9.1.1
RP-190227
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18-21, 2019

## Slide 2: Summary of NR V2X SI
100% completion is proposed in the status report.
  RAN1/2/3 concluded the completion of the study.
  TR 38.885 v2.0.0 is submitted to RAN.
NR V2X study scope
  Sidelink design
  Uu enhancement for advanced V2X use cases
  Uu-based sidelink resource allocation/configuration
  RAT/interface selection
  QoS management
  In-device coexistence of NR sidelink and LTE sidelink for ‘not co-channel’ scenario
Conclusion of the SI
  It is feasible to support advanced V2X services over the NR PC5 interface and the NR Uu interface.
    Remote driving use case was studied in the URLLC SI.
    Several solutions are recommended for the normative work.
    Noted that V2X solutions can be used for public safety when the service requirements can be met.

## Slide 3: Solutions recommended from NR V2X SI
NR sidelink design
  Sidelink signals and channels
  Resource allocation
    Mode 1 (scheduling from BS) and mode 2 (selection at UE)
  Synchronization mechanism
  Sidelink procedures including
    Power control, HARQ, channel measurement and feedback, congestion control
    MAC/RLC/PDCP/SDAP/RRC protocols over the PC5
  A common design for FR1 and FR2 (PT-RS in FR2)
Uu enhancement
  Multiple UL configured grants (also studied in the URLLC SI)
  reporting of UE assistance information to gNB
    can be used for sidelink scheduling as well
QoS management
Cross-RAT management (LTE Uu managing NR SL, NR Uu managing LTE SL)
  Not using physical signalling
Network interface enhancement
RAT/interface selection
In-device coexistence solutions

## Slide 4: Discussion and proposal
Discussion points
  The feature of multiple UL configured grants was also studied in the URLLC SI.
    RAN can discuss the best way of specifying this feature.
    It is suggested to consider
      Proper handling V2X characteristics (e.g., period/offset variation, high mobility, …)
      Similarity to gNB scheduling sidelink using multiple configured grants
  5GAA requested more visibility for 3GPP V2X specifications [1].
    A stage-2 specification can be created to provide the overall description of LTE and NR sidelink solutions for V2X, referencing the corresponding section/specification of each sidelink function.
  5GAA requested to support 2 RX antennas in NR sidelink in FR1 [2].
    Current RAN1 assumption was made before the 2 RX vehicle antenna exception.
    RAN can provide guidance so that the request can be addressed in RAN4 work during the WI phase.
A WID is submitted in [3].
  Approve the WID to start the normative work.

## Slide 5: References
[1] RP-190037 LS on V2X specification visibility in 3GPP 5GAA WG4
[2] RP-190038 LS on 2Rx Antennas for NR V2X Sidelink 5GAA WG4
[3] RP-190226 New WID on NR-based V2X LG Electronics, Huawei