## Slide 1: Motivation paper for new SID on NR/WLAN Convergence
Intel Corporation
RP-190365

## Slide 2: Background 1/2
LTE supports various options for WLAN integration, interworking and aggregation at RAN level
RAN-assisted WLAN interworking
RAN-controlled WLAN interworking
LTE/WLAN Aggregation (LWA)
LTE/WLAN Radio Level Integration with IPsec Tunnel (LWIP)
Observation: NR currently lacks WLAN support, which is available in LTE

## Slide 3: Background 2/2
5GC supports various options for WLAN integration at core network level as untrusted/trusted non-3GPP access
Untrusted WLAN in Release-15
Trusted WLAN in Release-16
Traffic splitting, steering, switching between 3GPP access and non-3GPP access in Rel-16 (ATSSS)
Observation: WLAN integration into 5GC does not support tight convergence at RAN level

## Slide 4: Motivation (1/2)
Enterprise networks
Large influx of mobile devices in enterprises create need for comprehensive management and seamless connectivity for these devices
Most traffic in enterprise networks goes over WLAN
Little to no integration between cellular and WLAN
WLAN network management increases enterprise OPEX
Little penetration of cellular operators into enterprise
Observation: Enterprise networks present growth opportunity for cellular operators and can benefit from convergence with NR

## Slide 5: Motivation (2/2)
Benefits of RAN level convergence compared to interworking at 5GC
Enables Non-Public Networks (NPN), e.g. Industrial, Factory, etc. deployments with unlicensed spectrum (e.g. WLAN)
Provides common management for 3GPP and WLAN networks
Throughput gains, latency reduction, faster mobility, better network utilization
  Faster response to changing channel conditions
Lower network deployment and device cost
Lower backhaul overhead (if packet duplication is needed) as single copy of data traverses between 5GC and RAN

## Slide 6: Scenarios
Devices: Dual radio (NR and WLAN), where cellular or Wi-Fi can be the anchor
1) MNO deployed NG-RAN, WLAN and 5GC
2) MNO deployed NG-RAN and enterprise deployed WLAN, MNO deployed 5GC
3) Enterprise deployed NG-RAN, WLAN and 5GC
DN
5
GC
NG
-
RAN
WLAN
UE
Notes: Add a diagram?

## Slide 7: Study Item Scope
Traffic steering, switching, aggregation, splitting, retransmission and duplication mechanisms (RAN2)
Cellular and WLAN anchor point
Cellular anchor – scenario 1, similar to LWA/LWIP
WLAN anchor – scenario 2, gives more control to enterprise
Air interface user plane and control plane protocol aspects (RAN2)
Network interface user plane and control plane protocol aspects (RAN3)
Measurement and reporting (RAN2)
Coordination with SA2 and IEEE/WFA, as needed
Notes: Retransmissions, duplication