## Slide 1: Motivation for new WI proposal on intra-band non-contiguous CA requirements for FR1 Huawei, HiSilicon
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18-21, 2019
Document for: Discussion
Agenda Item: 9.1.5
RP-190387

## Slide 2: Justification
Some FR1 non-contiguous CA band combinations were proposed in Rel-16 basket WI. However, the general non-contiguous CA requirements for FR1 are not specified in Rel-15 specification.
In RAN4#89, a draft Rel-16 CR to introduce intra-band contiguous and non-contiguous CA for <2700MHz was endorsed in R4-1816226. Since some operating bands >2700MHz are also proposed recently to support non-contiguous CA, the corresponding requirements shall also be specified in the Rel-16 specification.
According to usual approach adopted in RAN4, the general CA requirements are not discussed under the basket WI. As it’s not appropriate to follow up and organize discussion under TEI agenda for a specific feature, a WI should be established to facilitate the study of NC CA general requirements.
Based on the agreement in RAN4#90, this WI is specific to DL NC CA which addresses the scope not covered by the endorsed CR in R4-1816226.

## Slide 3: Objective
Specify the general RF requirements for FR1 DL non-contiguous CA with two downlink sub-blocks for operating bands >2700MHz, which includes Rx requirements for non-contiguous CA.
  The Rx requirements for DL non-contiguous CA include REFSENS, maximum input level, ACS, blocking, spurious response, wide band intermodulation and spurious emissions, etc.
The band specific requirements which are not covered by the basket WI for intra-band non-contiguous CA shall be studied under this WI. These band specific requirements for n77(2A) and n78(2A) will be specified under this WI.
The intra-band NC CA can be release independent from Rel-15 The non-contiguous CA band combination specific requirements, e.g. operating band information, BCS, etc. are not included in this WI, which shall be studied in corresponding basket WIDs.