## Slide 1: Motivation for a new NR band covering the 40-43.5 GHz range
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN Meeting #83
Shenzhen, China, 18 – 21 March, 2019
RP-190473
Document for: Approval
Agenda item: 9.1.5

## Slide 2: Background
WRC-19 agenda item 1.13, Resolution 238 (WRC-15) identifies 37-40.5 GHz, 42.5-43.5 GHz and 40.5-42.5 GHz among other as IMT candidate bands
RAN4 has specified Bn260 (37-40 GHz) in Rel-15 and previously discussed a band covering 40.5-43.5 GHz (tentative), hence the range 40-40.5 GHz would not be covered
For WRC-19 discussions, important that 3GPP bands cover the entire 37-43.5 GHz range
APT members support identification of the frequency bands 37-40.5 GHz, 40.5-42.5 GHz and 42.5-43.5 GHz
  Regulators also consider 3GPP: e.g. the Japanese administration is considering a possibility of 37 - 40 GHz for NR since 3GPP specifies an operating band covering this range (this administration also supports the identification of the entire range 37-43.5 GHz for IMT)
CEPT will not oppose a global IMT identification for the full 37-43.5 GHz range
The CITEL preliminary proposal is support of an IMT identification for the whole range 37-43.5 GHz

## Slide 3: Justification
From the WRC-19 preparations, it is evident that many administrations across all ITU regions are interested in the allocation of the whole or part of the 37-43.5 GHz frequency range to mobile services. Therefore, operating bands covering the entire 37-43.5 GHz should be specified by 3GPP in order to accommodate operations in any part of this range
The range 37-40 GHz is already covered by the existing Band n260 (37-40 GHz) specified in Rel-15. It is necessary to specify a new band in Rel-16 to cover the rest of the range 40-43.5 GHz
  the band number n259 is not currently in use and is proposed as the frequency band indicator
The lower limit of the band is tentative and to be considered further during the WI phase, but the lower limit must be ≤ 40 GHz
  consider potential benefits of an overlap with Band n260

## Slide 4: Objective and time plan
The purpose of this work item is to specify a new NR TDD operating band, i.e. Band n259, covering at least the range 40-43.5 GHz taking into account the potential benefits of an overlap with Band n260. The lower limit of the band will be further analysed and decided by considering potential spectrum allocations in different regions, operator demands and RF implementation but should not exceed 40 GHz
The objectives (core) are to define:
  Determine the lower limit of Band n259
  Transmitter and receiver characteristics requirements for the UE (38.101-2)
  Transmitter and receiver characteristics requirements for the BS (38.104)
Completion by Dec 2019
RAN4 led