## Slide 1: WF on the scope of R-16 RRM and Demod work in RAN4
Intel
3GPP TSG-RAN #83 Meeting
Shenzen, China, 18-21 March 2019
RP-190659

## Slide 2: R16 NR RRM/Demod WI proposals
Summary of WI proposals with NR RRM/Demod scope
  Rel-15 leftover issues
    WI: NR requirement work continuation in Rel-16 (Nokia, RP-190455)
    WI: NR RRM requirements enhancement (ZTE, RP-190211)
    WI: NR performance requirement enhancement (CTC, RP-190258)
    WI: CSI-RS based L3 measurement requirements (Huawei, RP-190397)
    WI: NR RRM requirement improvement (CATT, RP-190454)
  New requirements
    SI: NR measurement gap enhancement (Intel, RP-190243)
    WI: NR support for high speed train scenario (CMCC, RP-190317)
    SI: Supplemental uplink usage of FR2 spectrum (SA and NSA) (Apple, RP-190356)

## Slide 3: Agreed WF in RAN4#90
In RAN4 #90 meeting, WF[1] on R15/R16 NR RRM scope was approved
Feature/requirements which were confirmed to be specified in R16 in WF[1]
  The requirements for LTE SRS carrier switching and NR SRS carrier switching will be specified in Rel-16.
  The RRM requirements for EN-DC and NE-DC related to LTE euCA will be specified in Rel-16
  The requirements for multiple SCell activation/de-activation will be specified in Rel-16
  The RRM requirements for CGI reading with autonomous gap will be specified in Rel-16.
  The CSI-RS based L3 measurement requirement will be specified in Rel-16.
Feature/requirements which were confirmed to be FFS in R16 in WF[1]
  Whether to specify RRM requirement related with inter-band FR2 scenario or independent beamforming on different FR2 CCs will be discussed in Rel-16
  Whether to specify the requirements for NR SRS antenna port switching will be discussed in Rel-16.
  The second pair of BLER for RLM would be discussed in R16.
  The requirement for NR-DC SFTD is not to be specified in Rel-15

## Slide 4: Scope of Rel-16 NR RRM requirements (1/3)
Specify RRM requirement of SRS switching requirements for NR SA, NR-DC, EN-DC and NE-DC including
  Delay and interruption requirement of the following cases
    LTE SRS carrier switching impacting NR CC
    NR SRS carrier switching impacting LTE CC
    NR SRS carrier switching impacting NR CCS
Specify the interruption requirements for EN-DC and NE-DC related to LTE euCA
Specify RRM requirements of multiple Scell activation/deactivation in both FR1 and FR2
Specify CGI reading requirements with autonomous gap for NR

## Slide 5: Scope of Rel-16 NR RRM requirements (2/3)
Specify RRM requirements of CSI-RS based L3 measurement
  Gap pattern of CSI-RS based L3 measurement if needed
  CSI-RS based intra-frequency and inter-frequency definition
  Intra-frequency and inter-frequency measurement requirements
  Evaluate and specify CSI-RS based L3 measurement accuracy
  Specify the RRM test cases corresponding to the core requirements
  Study if necessary to introduce new UE measurement capability, including number of frequency layer and number of cells etc., for CSI-RS based measurement
  Study if necessary to specify the CSI-RS based handover requirements
  Study and compare the time tracking performance, from CSI-RS based L3 measurement perspective, between the following two options
    CSI-RS based
    Other RS based
    Note: study on the potential impact on other WG

## Slide 6: Scope of Rel-16 NR RRM requirements (3/3): study phase
Study to introduce RRM requirements for NR SRS antenna port switching in FR1 and NR SRS switching across panel in FR2
Study to introduce second pair of BLER for RLM enhancement
Study to introduce ANR measurement requirement with autonomous gap (LS R2-1902736)
Study to introduce inter-band CA requirement for FR2
  UE measurement capability,
  Scell activation requirement,
  interruption requirement
Study the feasibility to introduce Beamforming related enhancement with independent Rx beam for inter-band CA, including
  cell detection/measurement requirement,
  beam management requirements,
  Scell activation requirement,
  interruption requirement,
  scheduling restriction requirement ,

## Slide 7: Scope of Rel-16 NR Demod requirements (1/2)
    URLLC requirements
      BS side: PUSCH requirements with 10-5 BLER test metric
      UE side:
        PDSCH requirements with 10-5 BLER test metric
        CQI reporting requirements for the CQI table corresponding to 10-5 BLER target
        PDSCH requirements for DL pre-emption indication
    Interference-aware receivers for FR1
      BS side:
        PUSCH requirements with enhanced receivers for handling co-channel inter-cell interference.
          LMMSE-IRC or interference pre-whitening can be considered as reference receiver
        Study to introduce PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference.
          For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
      UE side:
        PDSCH requirements with enhanced receivers for handling co-channel inter-cell interference.
          LMMSE-IRC or interference pre-whitening can be considered as reference receiver.
        Study to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-stream interference for SU-MIMO.
          Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
    CA and EN-DC requirements
      UE side: PDSCH normal demodulation requirements and CA/EN-DC specific requirements, e.g, soft buffer management, power imbalance.
    PDSCH and CSI requirements with the number of Tx ports larger than 8 and upper to 32
    Notes
      Other requirements are not precluded
      Down-selection and/or prioritization among the requirements can be done in the WI stage

## Slide 8: Scope of Rel-16 NR Demod requirements (2/2): study phase
  Interference-aware receivers
      BS side
        Study to introduce PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference. For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
    UE side:
        Study to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-stream interference for SU-MIMO. Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver

## Slide 9: Scope of R16 High speed train WI (RRM and Demod)(1/2)
Target speed is [500 km/h], carrier frequency is up to 6GHz.
Scenarios and channel model includes
  HST-SFN scenarios, e.g. the channel mode captured in Section B.3A of 3GPP TS 36.101
  HST scenarios with high Doppler frequency, e.g. the channel mode captured in Section B.3 of 3GPP TS 36.101
  TDL channel with high Doppler frequency
  Other deployment scenarios are not precluded
Investigate and specify the UE RRM core requirements
  Cell reselection requirements
  Cell identification requirements when DRX is used.
  Measurement delay requirements when DRX is used.
  Measurement accuracy requirements
  If needed other requirements are not precluded
Investigate and specify the RRM performance requirements of measurement accuracy.

## Slide 10: Scope of R16 High speed train WI (RRM and Demod)
Specify the RRM test cases for:
  Cell reselection requirements
  Cell identification requirements when DRX is used.
  Measurement delay requirements when DRX is used.
  Measurement accuracy requirements
  Other test cases are not precluded if the core requirements are specified.
Specify the UE demodulation requirements and test cases for NR PDSCH
  Other requirements are not precluded if needed.
Specify the BS demodulation requirements and test cases for NR PUSCH
  Other requirements are not precluded if needed.

## Slide 11: WF on rel-16 scope prioritization
Prioritized items to be approved in Rel-16 include
  Identified Rel-15 leftover RRM issues in slide 4 and 5
  Identified Rel-16 demod issues in slide 7
  HST WI in slide 9 and 10

## Slide 12: Reference
[1] R4-1902032, Way forward on R15 NR RRM scope, Intel