## Slide 1
Motivation for NR to Support local LMF in RAN
CMCC
3GPP TSG RAN WG Meeting #83
Shenzhen, P.R.China, Mar. 18th -21st, 2019
Document for: Discussion
Agenda Item: 9.3.13
RP-190323

## Slide 2
Operators requirements and use cases
NR positioning requirements of operators:
  Support of low latency and high performance LCS
    For use cases related to vehicular positioning and positioning of objects in a factory
  Allow the RAN to have UE location
    For complementing MDT, better beamforming, and indoor/outdoor classification, etc.
  Improve the utilization rate of radio resources
    Through dynamic coordination of position resources among the neighbouring gNBs
  Support of flexible deployment
    Distributed deploy the location management function in NG-RAN, e.g. near UEs, to reduce signalling latency and overhead
Observation1: NR positioning architecture in Rel-15 cannot fully satisfy the requirements of operators and aforementioned use cases.

## Slide 3
Back ground
SA2 has carefully studied the feature “local LCS management function in NG-RAN” and recognized it as one of the effective solution to resolve “Key Issue 3: Support of low latency and high performance LCS”. The related conclusion is as follows:
  23.731 V16.0.0 section 7.8 “Evaluation of Solutions for Key Issue #3”:
    The low latency and high performance can be achieved by:
    allowing location management functionality supported in NG-RAN, as supported by Solution 15, 23, 26 and 28.
  23.731 V16.0.0 section 8.8 “Conclusions for Key Issue #3”:
    The following means to achieve low latency and high-performance location estimation can be considered in R16 normative work development:
    NG-RAN node enhanced with the support of location management functionality may be selected to perform UE positioning locally in the RAN under the condition that RAN WG(s) concludes that NG-RAN supports location management functionality.
Observation 2: SA2 has already studied the feature with local LCS management function in NG-RAN and recognized it as one of the effective solutions to support low latency and high performance LCS.

## Slide 4
RAN2 conclusion on architecture
Based on SA2 conclusions and suggestions, RAN2 has also carefully analyzed the pros and cons of the architecture “local LCS management function in NG-RAN”, and finally made the following conclusion in RAN2#105 meeting after exhaustive discussions:
    From RAN2 perspective, we conclude that this option is recommended for normative work, provided the concerns raised in the study phase are addressed
    The concerns mentioned above are about security risk and latency gains. However,
    The security aspects should be assessed by SA3 as it is out of RAN scope.
    The latency gains have already been evaluated and confirmed by SA2.
      23.731 section 6.26.5 (solution 26): Since the LMF related capabilities are supported in NG-RAN, the signaling transmission process via 5GC can be avoided, the solution can greatly improve the latency performance of the location service.
      23.731 section 6.28.5 (solution 28): The proposed solution enables timely delivery of the high accurate UE location estimation by reducing latency introduced at the mobile backhaul for the UE positioning. The latency is reduced to the largest extent.
      In our view, the latency gain is not just depending on the number of signalling reduced but also depending on the deployment. E.g. if the serving LMF is very remote from the AMF, the latency for AMF to LMF signalling are sure to be costly.
Observation 3: RAN2 has already studied and recommended to support LMC in RAN in NR positioning in Rel-16.
Observation 4: The security and latency issues is in the scope of SA WGs instead of RAN WGs.

## Slide 5
RAN3 conclusion on architecture
Due to the fact it is challenging to review, discuss, and conclude on all topics related to the Study Item on NR Positioning in one meeting, RAN3 could only make the following conclusion:
    Regarding location management functionality in RAN, RAN3 could not reach a common understanding on any recommendation.
    But they have already identified the potential enhancements when defining future work for NR positioning, as described in the agreed pCR(R3-191089).
Observation 5: RAN3 has already identified the potential enhancements for the architecture with LMC in RAN, though they have no time to discuss in NR positioning SI phase.
TP for TR 38.855
9.x Architecture procedure and protocol High Layer aspects
Regarding location management functionality in the NG-RAN, the location of the LMC function should be further considered, including possible new interface(s), impact on existing protocols, and coordination with the LMF in the 5GC.

## Slide 6
Our proposals
Proposal 1: Specify Local LMC in NG-RAN in Rel-16 NR positioning WI.
Considering SA2 and RAN2 have carefully studied the architecture with LMC in NG-RAN and both recommended it to be considered in R16 normative work development, we propose: