## Slide 1
Motivation for New WID on Extension of Integrated Access and Backhaul (IAB) for NR
3GPP TSG RAN Meeting #84
Newport Beach, USA, June 3-6, 2019
Agenda Item: 8
Document for: Information
RP-191181

## Slide 2: Background
Rel-16 IAB aims at basic operations
  Architecture and protocol design
  IAB integration procedure
  Routing, BAP and BH configuration
  CP and UP data transmission via IAB
  Topology support:
    Spanning Tree (ST) and Directed acyclic graph (DAG)
    Intra-Donor adaptation is prioritized
The following cannot be supported in Rel-16
  Mobile IAB
  Topology support: Mesh
Some functionalities in Rel-16 may not be completed due to time constrains e.g.
  Topology adaptation between IAB donors
  Mechanisms for efficient control signaling transmission

## Slide 3: Mobile IAB
In the subway, bus or train, the instantaneous traffic is moving. IAB node in the vehicle is economical comparing with deploying so many base stations or fixed IAB nodes along the route.
Poor indoor coverage: due to large fluctuation of NR frequency band, especially FR2, the coverage inside various vehicles is poor compared to the outdoor coverage. The backhaul link served by the mobile IAB node has better link quality and large bandwidth
Mobility procedure is frequent for users in the vehicle. Due to multi-hop property of IAB network, the latency for handover could be improved with group mobility for mobile IAB.
Mobile IAB

## Slide 4: Mesh
Wireless backhaul links are vulnerable to blockage due to e.g. moving objects such as vehicles, seasonal changes, or infrastructure changes.
Traffic variations can create uneven load distribution on wireless backhaul links leading to local link or node congestion.
To improve the coverage, achieve load balancing and reliability, Spanning tree (ST) and Directed acyclic graph (DAG) are included in Rel-16 for IAB topologies. ST and DAG have their limitations e.g. limited route redundancy, uneven load distribution.
Mesh-like optimizations will be beneficial e.g. to support ad-hoc deployments in case of emergency services, disaster relief, military etc.
  Each IAB node can have more redundant routes towards the IAB donor
  Improve the load distribution among different IAB nodes
  More robust to the link failures

## Slide 5: Rel-16 Leftovers
Intra-Donor adaptation is prioritized. It’s highly possible that Topology adaptation between IAB donors cannot be completed. To assure the robust to the link failures in various deployment scenarios, topology adaptation between IAB donors is also important.
In Rel-16, we focused on to make IAB workable due to tight timeline. Considering the multi-hop property, it is possible to do some optimizations to improve the efficiency of IAB:
  Control signaling latency reduction: RRC protocol is in IAB Donor. In case of multi-hop, the control plane signalling has to be transmitted via multi-hop to the IAB Donor. This may not be acceptable for URLLC services.
  QoS management: the QoS management of IAB network is controlled by IAB donor CU with no/little IAB node involvement. The UE DRB/BH RLC CH may be failed to be set up/modified or be released due to inappropriate QoS parameter setting
  Incomplete flow control scheme: F1-U is reused for end-to-end flow control, while hop-by-hop flow control is focused on the congestion avoidance. E.g.
    if the packet lost over wireless links and that over the wired link can be differentiated, the lost packet doesn’t need to be retransmitted from the IAB Donor-CU.
    Hop to hop radio link outage/resume could be supported which is not possible in Rel-16.
  Low-latency scheduling optimisations: May not be prioritized in Rel-16, but it is important for latency reduction.

## Slide 6: Objectives for IAB Extension in Rel-17
The work item should specify techniques to support mobile IAB, mesh based optimization, and enhancements to Rel-16 baseline .
  The detailed objectives for mobile IAB are:
    Support of service continuity for UEs served by mobile IAB. The following scenarios should be covered:
      IAB mobility between upstream intermediate IAB-nodes within the same IAB-donor.
      IAB mobility between two IAB donors connects to 5GC.
      IAB mobility between IAB-Donors working in different mode i.e. SA or NSA.
      IAB mobility between two IAB-Donors working in NSA mode.
    Specify group mobility mechanisms to reduce the latency and signalling load.
  The detailed objectives for mesh topology for multi-hop backhauling enhancements are:
    Specify procedures to configure multiple paths from IAB-donor to an IAB node.
    Specify control plane signalling for transmitting assistant information between IAB nodes to support route selection.
    Specify procedures to dynamic change the route and/or the role of IAB nodes.
  The detailed objectives for enhancements to Rel-16 baseline include:
    Specify mechanisms for efficient control signalling transmission.
    QoS management optimisation
    Hop-by-hop flow control enhancement
    Low-latency scheduling optimisations

## Slide 7
Thanks!