## Slide 1: SON Enhancements in Rel-17
Source: Ericsson
Agenda: 8
RP-191370

## Slide 2: Introduction
In Release 16, MDT, L1/L2 measurements for KPI monitoring and LTE like-SON functions are included.
  Depending on the time availability in Rel-16 WI, some of the following SON functions will be standardized in Rel-16
    Capacity and Coverage Optimization
    PCI selection
    Mobility optimization
    Load Sharing and Load Balancing Optimization
    RACH Optimization
    Energy Saving
For Release 17, we should consider SON functions needed for NR specific operations.
  SMTC Related Error Reporting
  Enhanced CCO Data Collection
Local RRM policy container for idle mode UEs
Part of the time units for Rel-17 SON should be allocated for configuration and optimization challenges based on first deployments.

## Slide 3: SMTC Related Error Reporting
Identify problems by checking SMTC.
UE assisted detection of PCI collision
  SSBs of a given PCI not arriving in ascending order could indicate two cells transmitting the same PCI.
  SSBs of a given PCI in the SMTC duration not arriving in correct nominal locations could indicate two cells transmitting the same PCI.
UE assisted detection of sub-optimal SMTC configuration
  A different SSB index than 1 in the beginning of the SMTC could indicate non-aligned SMTC configuration.
Report identified problems in a SMTC Error Report.
1
2
3
1
1
2
5
5
Network
UE
Error report reqt
Error report resp

## Slide 4: Enhanced CCO Data Collection
Motivation
  Measurement reporting procedure in NR is simillar to LTE with some enhancements related to beam reporting.
  The measurement report size in NR could be larger and potentially the rate of degradation of the SINR in mmW bands could be very rapid.
  Sending larger measurement reports in poorer radio condition is challenging.
Enable separate triggering points for measurement logging and measurement reporting by introducing new reporting configuration options.
Network
UE
Measurement configuration
Certain event condition satisfied
UE performs logging of measurements
Certain other event condition satisfied
Measurement report

## Slide 5: Local RRM policy container
Motivation
  Learning of the UE specific RRM policies gives better adaptation to the UE's environmental and mobility factors
Introduce the UE specific and vendor specific RRM policy container that can be retrieved at the transition.