## Slide 1: Release 17 Focus Area RAN aspect of E2E NW Slicing
RP-191467 4 June 2019
KDDI Corporation, HPE

## Slide 2: Justification
NW Slicing is one of the key functionalities of 5G. It is highly significant to meet diversifying needs of the times.
However, the specifications ever defined still remain intra-domain discussion, e.g., mobile core or transport. The discussion in the communities related to the management domain is just beginning.
The operators should be able to provide guaranteed SLA based on the customers’ requirements in the E2E manner.
GSMA has active discussion of the NW slicing under the NEST taskforce which is the umbrella of Future Networks Programme. In the NEST taskforce, End to end network architecture discussion is one of the working packages.

## Slide 3: Justification
NW Slicing

## Slide 4: Justification
To ensure the SLA per slice profile (i.e., use case) in the E2E manner, enhancements of NW slicing from RAN perspective should be studied
There is a lack of the way of management to guarantee the SLA in RAN domain
  There is no way of verifying whether the KPI of the NW slice is met in RAN domain
  The indication functionality for the admission control or the resource management of slice(s) is required
U-plane traffic resource management in RAN does not reflect NW slicing concept from the E2E traffic resource management perspective
  The granularity of U-plane traffic management is per QoS flow
  There is no mapping between the NW slice and the QoS flow in the access network between E and RAN
RAN sharing we know in 4G will evolve to 5G , and with slicing becoming de facto standard , carriers sharing a 5G RAN would use slices and want to have an API allowing managing of that RAN subnet slice

## Slide 5: Objective
Items to be considered but not limited in these;
  The management method to guarantee the SLA;
    API definition to guarantee the customer’s SLA, to enable admission control per slice or context awareness
    It is assumed that this API is not used for exposure to 3rd Parties, but only for operators domain (e.g., RAN controller under definition at O-RAN Alliance, MEC servers or operator proprietary O&M tools)
    Examples of information to be exposed; traffic resource allocation, current status of the number of active UEs
  Traffic management in AN
    Mapping between 5QI/SPID and S-NSSAI – AN resources and PDU session(s)
    See next slide
  RAN sharing aspect
    From the frequency band perspective, the small cell deployment is much more essential in 5G RAN
    RAN Network Slicing enhancement should be considered from the RAN sharing in 5G era

## Slide 6: Traffic management in AN
Operators can configure the slice instance based on the priority which reflects the customer SLA and their policy. This priority can be applied to the PDU sessions which is mapped to the corresponding slice(s)
Slice #1 SST value = 1 (eMBB)
Operator defined priority: Mid
QoS flow#1 5QI=10
QoS flow#2 5QI=1
QoS flow#3 5QI=6
PDU Session#1
PDU Session#2
Slice #2 SST value = 2 (URLLC)
Operator defined priority: High
QoS flow#1 5QI=10
QoS flow#2 5QI=1
QoS flow#3 5QI=6
PDU Session#1
PDU Session#2
These QoS flows have same 5QI even though slice priority is different
There is no way of differentiating QoS flows with same 5QI value but being mapped to different slices

## Slide 7: Summary
NW Slicing is one of the key functionalities of 5G
From the operators point of view, to provide guaranteed SLA based on the customers’ requirements in the E2E manner is highly required
From RAN network slice aspect, enhancement should be discussed in Rel-17 for example;
  The management method to guarantee the SLA
  Traffic management in AN

## Slide 8
Thank you!