## Slide 1: Summary of email discussion on NR coverage enhancement
China Telecom
September 2019
3GPP TSG RAN Meeting #85
Newport Beach, USA, September 16-20, 2019
Agenda: 8.1.5

## Slide 2: Email discussion on NR coverage enhancement
In RAN#84, NR coverage enhancement was identified as one RAN work area for Rel-17 and RAN level email discussion was assigned with the following guidelines:
  Clarify requirements for all relevant deployment scenarios focusing on extreme coverage (not including LPWA). Data rate target FFS.
  Start from Rel-16 email discussion outcome
  Include both indoor as well as wide area

## Slide 3: Email discussion on NR coverage enhancement
We propose the email discussion comprises two phases:
  Phase 1 (till RAN#85): Further clarify the requirement and deployment scenarios starting from initial email discussion in Rel-16 and outcome of link budget evaluation for ITU submission.
  Phase 2 (from RAN#85 to RAN#86): Scope out the objectives for the SID or WID.

## Slide 4: Email discussion on NR coverage enhancement
41 companies, including 18 operators
CTC, CMCC, China Unicom, DCM, Softbank, Verizon, AT&T, Orange, Vodafone, KT, Telstra, Bell, Sierra Wireless, Rjio, BT, Charter Communications, Dish, Telefonica, Huawei, ZTE, Samsung, CATT, Nokia, Ericsson, QC, Hisilicon, MTK, Spreadtrum, vivo, OPPO, xiaomi, TCL, IITH, IITM, Tejas, CEWIT, FUTUREWEI, Lenovo, Motorola, Nomor Research, LG

## Slide 5: Scenarios for FR1
Indoor scenario
  Outdoor gNB serving indoor UE : 37 companies, including 16 operators thought it should be taken into account.
  Indoor gNB serving indoor UE: 4 companies, including 3 operators thought it should be considered.
Rural scenario
  Rural scenario: 37 companies, including 16 operators thought it should be taken into account.
  Extreme long distance coverage: 6 companies, including 3 operators, thought it should be part of rural scenario.
Other scenarios: 3 operators thought urban/ dense urban needs to be considered. 2 companies raised the issue of coverage hole. 3 companies, including 1 operator, mentioned the scenario with fixed UE or with very low speed.

## Slide 6: Services for FR1
VoIP: 37 companies, including 17 operators, thought VoIP is the fundamental service and the coverage should be enhanced.
eMBB: 38 companies, including 17 operators, thought eMBB should also be taken into account.
Target data rate of eMBB
  11 companies proposed that the target data rate should be higher than LTE. 17 companies provided the target data rate. The target data rate depends on the scenarios.
  For indoor or urban scenario, most companies proposed that the target data rate for UL should be at least 1~2 Mbps; while several companies proposed that the target data rate for DL should be about 10Mbps.
  For rural scenario, the target data rates of about 100kbps for UL and 1Mbps for DL were proposed.
  The target data rates for extreme long distance coverage and fixed services were also mentioned.

## Slide 7: Channels for FR1
30 companies, including 12 operators, thought both DL and UL should be taken into account. 5 companies thought which channels should be considered depends on the evaluation results.
10 companies proposed the coverage of PUSCH should be enhanced. 5 companies proposed the coverage of PUCCH should be enhanced. Enhancements on other channels, such as PDSCH/PDCCH/PRACH were also mentioned by several companies. 6 companies thought all the channels should be taken into account.

## Slide 8: Conclusions for FR1
Proposal 1: Indoor scenario (outdoor gNB serving indoor UE) and rural scenario should be taken into account for coverage enhancement for FR1.
Proposal 2: VoIP and eMBB service should be taken into account for coverage enhancement for FR1.
Proposal 3: Both DL and UL should be taken into account for coverage enhancement for FR1. And coverage enhancement for UL should be prioritized.

## Slide 9: Scenarios for FR2
Indoor scenario: 38 companies, including 17 operators, thought indoor scenario should be taken into account. Among them, 14 companies, including 6 operators, thought indoor scenario refers to indoor gNB serving indoor UE; while 5 companies, including 3 operators, thought indoor scenario refers to outdoor gNB serving indoor UE.
Urban/dense urban: 18 companies, including 8 operators, thought urban/ dense urban should be taken into account.
Fixed wireless access: 4 companies, including 3 operators, thought fixed wireless access also needs to be considered.

## Slide 10: Services for FR2
VoIP:
  15 companies, including 6 operators, thought VoIP is should be taken into account for FR2.
  19 companies, including 9 operators, thought VoIP is not the typical service for FR2.
eMBB:
  36 companies, including 15 operators, thought eMBB should also be taken into account.
  14 companies proposed that the target data rate for FR2 should be higher than FR1. 8 companies provided the target data rate. The target data rate depends on the scenarios.
  For indoor or urban scenario, it was proposed that the target data rate for UL should be several Mbps, while the target data rate for DL should be several dozens of Mbps.
  The target data rate for fixed wireless access was also mentioned.

## Slide 11: Channels for FR2
22 companies, including 9 operators, thought which channels should be considered depends on evaluation results, and expect thorough evaluation of the channels for FR2.
8 companies, including 5 operators, thought both DL and UL should be taken into account. And 9 companies thought all the channels should be taken into account.
5 companies proposed the coverage of PUSCH should be enhanced. 4 companies proposed the coverage of PUCCH should be enhanced. Enhancements on other channels, such as PDSCH/PDCCH, were also mentioned by several companies.

## Slide 12: Conclusions for FR2
Proposal 4: Indoor scenario (indoor gNB serving indoor UE) and urban/dense urban scenario should be taken into account for coverage enhancement for FR2.
Proposal 5: eMBB is considered for coverage enhancement for FR2.
Proposal 6: Both DL and UL should be taken into account for coverage enhancement for FR2. And which channels should be considered depends on evaluation results.

## Slide 13
Thank you！