## Slide 1: On switching period between two FR1 uplink carriers
3GPP TSG RAN Meeting #85
Newport Beach, USA, September 16-20, 2019
Agenda: 9.4.19
RP-191894
China Telecom
September 2019

## Slide 2: Background
UE RF requirements for switching period between two uplink carriers for FR1 was discussed in RAN4 #92 meeting:
      R4-1908584, Discussion on requirement for switching period between two FR1 uplink carriers, China Telecom, CMCC, China Unicom, KDDI, Orange
      R4-1908622, CR to TS 38.101-1: Switching time mask between 1Tx and 2Tx, China Telecom, CMCC, China Unicom, KDDI, Orange
      R4-1908623, CR to TS 38.101-3: Switching time mask between 1Tx and 2Tx, China Telecom, CMCC, China Unicom, KDDI, Orange
      R4-1910531, Ad-hoc minutes on switching period between two FR1 uplink carriers, China Telecom

## Slide 3: Motivation
Main benefits of 2Tx over 1Tx
  With the wide deployment of massive MIMO and the use of 16, 32 or 64 receiver antenna ports at NR BS, the operating SNR level for UL-MIMO can be significantly decreased. So compared to LTE, UL-MIMO with 2Tx is much more useful for NR.
  Given the use of 4Rx, 2T4R implementation on UE is more preferred than 1T4R for SRS antenna switching, which will improve the downlink MIMO performance.
  2Tx is linked to the potential support of 26dBm high power UE in practical.
Currently NR commercial UEs can support at most 2 concurrent uplink transmission chains in FR1, due to terminal cost, power consumption and heat dissipation issues.
Therefore, to enable 2 Tx on NR carrier together with EN-DC, SUL and UL CA, an efficient way is to introduce Tx switching between two uplink carriers.

## Slide 4: Possible UE behaviors for different lengths of switching periods
~0 us switching period:
  Implementation 1: 3 transmitters, 3 PAs, 3 independent power suppliers
35 us switching period:
  Implementation 1: Switch of the connections for the shared components, e.g., PLL, power supplier, PA module, filter, switch, etc.
140 us switching period:
  Implementation 1: PLL relocking and PA switching
  Implementation 2: 3 PAs with 2 ETs
900 us switching period:
  Implementation 1: whole BB and TX chain need to be retuned

## Slide 5: Proposal
Add the following objective in “RF requirements for NR frequency range 1” WI
  UE requirements for switching period between UL 1Tx carrier and UL 2Tx carrier for FR1

## Slide 6
Thanks!