## Slide 1: Views on Rel-17 Industrial IOT enhancement

## Slide 2: Background
The IIOT enhancement was agreed as one of Rel-17 Work Area in RAN#84 (RP-191551)
  E-mail consolidation will start after RAN#85
This material provides LG Electronics’ view on Rel-17 IIOT enhancement to facilitate e-mail consolidation.

## Slide 3: Proposed Scope: Throughput Enhancement
Use case
  Augmented Reality
  High data rate video streaming / professional video production
Requirements
  High data rate along with low latency
Challenges in Rel-16 IIOT
  Rel-16 IIOT focuses on PDCP duplication on more than 2 legs, which ensures ultra high reliability using Duplicate Radio Bearer.
  However, to support high data rate with ultra-low latency, split bearer operation should also be supported together with duplication.
Proposed objectives
  Duplication over split bearer
MCG
PDCP
RLC
RLC
RLC
RLC
SCG
Split bearer operation
Duplication
Duplication

## Slide 4: Proposed Scope: Critical Data Transmission
Use case
  Motion control
  Mobile robots
  Telecare
Requirements
  Simultaneous transmission of non-critical data and highly-critical data over the same link and to the same device.
Challenges in Rel-16 IIOT
  Packets belonging to a single TSN flow are transmitted through a single radio bearer, and there are no differentiation between those packets.
  However, the TSN flow may also contain critical packets, which need to be prioritized in radio transmission.
Proposed objectives
  Packet prioritization within a single TSN flow