## Slide 1: Discussion of the Scope of Rel-17 NR Positioning Enhancements
RP-191978
3GPP TSG RAN WG Meeting #85
Newport Beach, USA, Sept 16 – 20, 2019
Document for: Discussion
Agenda Item: 8.1.9
China Academy of Telecommunications Technology (CATT)

## Slide 2
Rel-16 NR Positioning SI (completed in RAN#83)
  Defined target regulatory and commercial performance requirements for Rel-16
  Defined three NR positioning evaluation scenarios (Indoor office, UMi, UMa) for system level analysis
  Concluded that it is feasible to achieve the target regulatory and commercial performance requirements for horizontal positioning accuracy for the evaluation scenarios
Rel-16 NR Positioning WI (on-going)
  Focuses on the RAT-dependent positioning techniques recommended by Rel-16 NR Positioning SI, namely, DL-TDOA, DL-AoD, UL-TDOA, UL-AoA, RTT and E-CID
R16 NR Positioning SI/WI

## Slide 3
Motivations of R17 NR Positioning Enhancements
5G positioning performance requirements [TS 22.261, TS 22.104]
Absolute positioning
  Horizontal: accuracy 10m to 0.3m with 95% confidence and 95% to 99.9% availability
  Vertical: 3m to 2m with 95% confidence and 95% to 99.9% availability
Relative positioning
  Horizontal: 0.2m with 95% confidence and 99% confidenceVertical: 0.2m with 95% confidence and 99% confidence
Time latency (time to first fix): from seconds to ms
  Target Rel-16 positioning performance (TR 38.855)
  Horizontal positioning error < 3m (80%) (indoor ) and < 10m (80%) (outdoor)
  Vertical positioning error < 3m (80) (indoor) and error < 3m (80) (outdoor)
  Time latency (time to first fix) < 1 second
Significant gap between R16 target positioning performance [TR 38.855] and 5G positioning performance requirements [TS 22.261, TS 22.104] in terms of positioning accuracy, latency, availability, and reliability.

## Slide 4
5G NR needs to support much more use cases of 2D/3D positioning with high accuracy, low latency and high reliability, e.g.,
  V2X positioning
  Idle and inactive UEs
  Factory/campus positioning
  IoT positioning
Many promising techniques were actually proposed during Rel-16 NR Positioning SI/WI but were not further investigated in Rel-16, e.g.,
  NR carrier phase based positioning
  Multipath mitigation techniques, such as LOS detection, multiple measurements reporting
  Corporative positioning
  Differential NR positioning
  Precise time/phase and frequency synchronization of the wireless network based on NR reference signals
  Phase difference of arrival based positioning
  Received signal waveform reporting
  NR Positioning for UEs in RRC_IDLE/INACTIVE modes
Motivations of R17 NR Positioning Enhancements

## Slide 5
Carrier phase positioning (CPP) is commonly in GNSS for cm-level positioning (e.g., RTK, PPP). CPP technique can also be used in NR for cm-level positioning based on NR PRS and/or NR carrier-PRS.
NR has a number of salient advantages over GNSS in CPP
  Has much higher receiving signal power
    Quicker phase-lock
  Allow flexible configuration for the transmission of reference signals
    Faster integer ambiguity resolution
    Better RF resource Optimization
    Lower implementation complexity
  Work in any environment where NR reference signal can be reliably detected, including the locations where GNSS signals are not available
NR carrier phase positioning

## Slide 6
High-accuracy positioning (with the velocity and heading) with very low latency are critical for V2X operation
Using multiple antennas, MIMO and large carrier bandwidth will increase AOA and TOA measurement accuracy and reliability for V2X positioning
Carrier phase positioning (GNSS CPP and/or NR CPP) can also be used together with other techniques (e.g., IMU) to support high-performance V2X positioning.
Cooperative positioning with the information exchange among UEs can improve V2X positioning performance
V2X Positioning
Vehicle B
Vehicle B
x
y
Vehicle A
A1
A2
B1
B2
Information Exchange

## Slide 7
Differential techniques are commonly used in GNSS positioning
  increase the positioning accuracy by one order of magnitude or more
Differential positioning can also be applied in NR positioning
  One (or more) receiver at a known location is used as the reference receiver
  The receiver estimates the error corrections for the neighboring TRPs
    e.g., RSTD errors caused by TRP time misalignment
  Estimated error correction are used by the location server or the UEs to eliminate the measurement errors for high-accuracy positioning
Differential NR Positioning
TRP 1
Reference
Receiver
TRP 2
TRP 2
Differential corrections
LMF
UE

## Slide 8
RAN1 centric objectives
  Identify the target commercial use cases (e.g., V2X) and the performance requirements for NR positioning enhancement according to 5G positioning services defined in TS 22.261 and TS 22.104
  Extend R16 NR positioning evaluation scenarios for evaluating the identified commercial use cases
  Investigate advanced techniques for positioning enhancements (e.g., carrier phase positioning, differential NR positioning, etc.) with the consideration of accuracy, availability, reliability, scalability, TTFF etc. The NR positioning enhancements to be investigated may include, but not limited to, the positioning techniques proposed during Rel-16 SI/WI
  Extend downlink and uplink positioning reference signals, and define new downlink, uplink, and sidelink positioning reference signals, for supporting the positioning enhancements
  Define UE and gNB positioning measurements supporting the positioning enhancements
  If necessary, define new physical-layer procedures to support UE/gNB measurements supporting the positioning enhancements
Objectives of R17 NR Positioning Enhancements

## Slide 9
RAN2 centric objectives
  Extend the functional interfaces, signalling and procedures including UE reporting, to support NR RAT-dependent positioning for the NR positioning enhancements listed in RAN1 objectives
  Define extensions of LPP and RRC protocols for supporting NR RAT-dependent positioning enhancements
RAN3 centric objectives
  Define extensions of high-layer protocols (e.g., LPPa, Xn) for supporting NR RAT-dependent positioning enhancements
RAN4 centric objectives
  Define corresponding core requirements for NR positioning enhancements
  Define corresponding performance requirements and test cases for NR positioning enhancements
Objectives of R17 NR Positioning Enhancements

## Slide 10: Potential Impacts on Other WGs
The Proposed work on Rel-17 NR positioning enhancements may have mutual impacts with
  SA work on the 5G location service architecture and enhancements (e.g., active SI on Enhancement to the 5GC LoCation Services-Phase 2 (SP-190452))