## Slide 1: Motivation for New WI on Efficiency Improvement of Data and Signaling Transmissions (EIDST)
CATT, CAICT
RP-191982
3GPP TSG RAN WG Meeting #85
Newport Beach, USA, Sept. 16 - 20, 2019
Document for: Discussion
Agenda Item: 8.2.5

## Slide 2: Outline
Motivations
Proposed work scope of EIDST

## Slide 3: Motivations – to think about the whole picture
Rel-15/16 NR work has put extensive effort to the following dimensions
More Bands
Spectrum Efficiency
Latency Reduction
FR2
Unlicensed band
LTE and NR DSS
…
Massive MIMO
Higher QAM
New channel coding
…
Mobility Enh.
DC/CA Enh.
RACH Enh.
…
It becomes increasing important to work on OTHER dimension with higher input-output ratio!
As we are approaching some of the physical limits, the room for improvement is less in the near future!
Efficiency Improvement of Data and Signaling Transmissions (EIDST)
Key idea – less redundancy over AI, based on compression, and signaling optimization

## Slide 4: Motivations – Data compression
Efficiency
  Data compression has proved efficiency improvement.
Harmonization
  Unified support of UDC for E-UTRA in EPS and 5GS, and also for NR, ensures consistent performance across multiple RATs and deployment scenarios.
Support of ENDC
  Without UDC support in NR PDCP, E-UTRA in Option 3x is less efficient than E-UTRA in Option 3a.
Mobility and Voice performance
  Mobility performance impacted without NR UDC, due to the need of an extra decompression/compression when going from E-UTRAN/NG-RAN to NG-RAN/E-UTRAN.
  Improved voice robustness with NR UDC in Option 3x.
Reduced Power Consumption
  Data compression to UL data leads to less UL transmissions, and in many cases relives the power constraint, which is more important in NR.
Motivations for new verticals use cases, e.g., IIOT and Video camera
  Cases with higher data redundancy can benefit more from compression
Benefits
Efforts
  Very limited effort: The support of UDC in NR and in E-UTRA in 5GS is a low-hanging fruit that requires minimal additions to NR UP.
See more details in RP-191149.

## Slide 5: Motivations – Data compression
It is well motivated and quite straightforward to support UDC in NR Rel-16 (for SA scenario).
Based on this, UDC can be further extended to more use cases.
  From SA case to DC case
  Also support UDC for UM data
Such extensions make UDC’s efficiency improvement available to more scenarios in Rel-17.

## Slide 6: Motivations – Signaling Optimizations
Leftovers from Rel-16 RACS WI can be further studied and supported in Rel-17.
  UL segmentation supported in Rel-16 only for UE capability signaling. This can be extended to other UL signaling.
  In DL, there are still several messages may have a large size, e.g. RRC reconfiguration message, RRC resume message. Segmentation similar as for UL can easily be applied to DL messages.
  Delta signaling (with UE capability ID) is studied in Rel-16, and it can be included as part of Rel-17.

## Slide 7: Motivations – Signaling Compression
Uplink Capability Signalling Compression (UCSC) is well studied, and its efficiency improvement is proved.
  Solution studied in UE capability signaling optimization SI, but not as part of WI as UDC is not yet available for NR UP.
  Evaluations (see R2-1900479 for details) show clear compression gain.
 | UE capability size (bytes) | Size reduction
Case 1 [3] | 3161 | 59%
Case 2 [2] | 1082 | 46%
Case 3 [4] | 300 | 30% - 50%
Table 1. UE capability size reduction by pure compression
 | UE capability size (bytes) | Size reduction
Case 1 [3] | 3161 | 98.8%
Case 2 [2] | 1082 | 98.3%
Table 2. UE capability size reduction by compression with dictionary

## Slide 8: EIDST – Proposed Rel-17 Work Scope
UDC enhancements for NR:
  Taking LTE UDC and NR UDC as baseline:
    Support UDC for more scenarios, including NR-DC, MR-DC cases.
    Support UDC for RLC UM mode data:
      specify a mechanism to support static dictionary, e.g., on a per service basis
Further signaling optimizations:
  Support of signalling segmentation for other UL RRC signalling than UE capability;
  Support of DL RRC signaling segmentation by using the similar mechanism as UL UE capability segmentation;
  Support of delta signaling with UE capability ID, to further lower the UE capability signaling size;
  Support of UL signaling compression, e.g. based on compression algorithm DEFLATE.
See WIDs in RP-191983