## Slide 1: Agenda Item: 8.1.14 Source: AT&T Title: RAN Enhancements for Localized User Plane Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #85 RP-192108
Newport Beach, USA: September 16-20, 2019

## Slide 2: Support for NR-based Non-Public Networks
Non-public networks are increasingly becoming the preferred option for many enterprises:
Need to keep the user plane data in the premise (e.g. security/edge computing)
Requires heavy infrastructure deployment as private networks require full gNB on premise (e.g. a full CU and DU)

## Slide 3: Public/Non-Public Network Shared Infrastructure
Another option is to support a CU/DU split where only DUs and Local Managers (LMs) are contained or deployed within the enterprise, while the CU is deployed outside the enterprise
    A NPN uses a CU-UP and CU-CP deployed outside the premise, in common with the public network
    Different DUs are used for the NPN and the public network
    PC5 interface can be used to allow for local traffic routing within the NPN
DU
DU
DU
CU
To core
LM
PC5
F1
Uu
Uu
PC5
F1
Uu
Control plane
Local traffic
Cellular traffic
Non public network
Public network

## Slide 4: Localized User Plane (LUP)
A further extension for Rel-17 is to support a control plane (CP) and user plane (UP) split between the Public Network and the NPN:
Multi-connectivity is used to provide CP and UP functionality to the NPN
The CU-UP for the NPN traffic can be localized within the private network to support security and edge computing considerations
The CU-UP for the public network traffic can remain off-premise (e.g. co-located with the CU-CP)
The CU-CP remains common for both the public and NPN users
Proposal: Rel-17 should support RAN architecture enhancements to support Localized User Plane for Public Network Integrated NPN (PNI-NPN)