## Slide 1
RAN4 Outgoing Chairman: Xutao Zhou
Status Report RAN WG4 to TSG-RAN #86
3GPP TSG RAN #86 RP-192363
Sitges, Spain, 9th Dec. 2019-12th Dec. 2019

## Slide 2: Executive Summary – RAN4 Chairman election
An election for the position of RAN4 Chairmen was held in RAN4 #93 meeting.
Result of the election (Two ballots)
Dr. Xiang (Steven) Chen (Futurewei Technologies / ETSI) was elected as the RAN4 Chairman.

## Slide 3: Executive Summary – NR
Rel-15 NR
  Still high load with Rel-15 NR maintenance in Q4’19
  Rel-16 RF Core maintenance
    Several open issues are finalized or moved to ongoing Rel-16 WIs
  Rel-15 NR RRM Core part maintenance
    Several issues to be finalized or dropped out of R15 in Q1’20 incl. one shot timing adjustment requirements
    RRM requirements TCI state switch of the CSI-RS for CSI reporting and spatial relation switch for uplink were agreed to be deprioritized in R15 and proposed to be considered in R16 (R4-1915937)
  Rel-15 NR Performance part maintenance
    Many RRM performance test cases defined
    UE Demodulation/CSI requirements finalized
    BS demodulation requirements finalized
  Expect reduction in number of CRs for R15 NR in Q1’20 but still need to reserve TUs for maintenance
    Rel-16 NR
  Good progress for Rel-16 NR WI/SI for both spectrum and non-spectrum.
  For selected Rel-16 WIs the completed level is low and it may be challenging to achieve completion with current TU allocation in Q1’20

## Slide 4: Executive Summary – LTE
LTE maintenance up to Rel-15
  Number of maintenance CRs for Rel-15 WI performance parts has been reduced.
Rel-16 LTE
  Good progress on Rel-16 LTE WIs for both spectrum related and non-spectrum related

## Slide 5: Statistics
Chart: 
| #90 | #90bis | #91 | #92 | #92bis | #93
Delegates | 372 | 324 | 387 | 266 | 298 | 382
Chart: 
| #90 | #90bis | #91 | #92 | #92bis | #93
Contributions | 2584 | 2774 | 2337 | 2576 | 2230 | 2886
Meeting | Date | Location | Host | Delegates registered/attendees | Documents requested/uploaded
RAN4 #92bis | 14th – 18th October 2019 | Chongqing , CN | CF3 | 370/298 | 2381/2230
RAN4 #93 | 18th – 22nd November 2019 | Reno, USA | NF3 | 439/382 | 3111/2886

## Slide 6: NR

## Slide 7: Completion of ongoing WI/SI
SI/WI to be completed
Action to RAN on addition of bandwidth for band n25:
    Endorsed CR packs are supposed to be approved in RAN #86 based on the approval of revised WID (RP-192401) on removing bandwidth 35MHz.
Title | SR | CR packs | Endorsed CR packs
Study on high power UE (power class 2) to EN-DC(1 LTE FDD band and 1 NR TDD band) | RP-19786 |  | 
Introduction of 2010-2025MHz SUL band for NR | RP-192585 | RP-193013 | 
Addition of 25, 30, and 40 MHz channel bandwidth for NR band n25 | RP-192785 |  | R4-193015 *
Addition of wider channel bandwidth in NR band n38 | RP-192809 | RP-193016 | 
Adding wider channel bandwidth support to band n75 | RP-192515 | RP-193017 | 
High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) | RP-192582 | RP-13019 | 

## Slide 8: NR – RAN4 led items

## Slide 9: FR1 UE RF
Almost contiguous allocation MPR was agreed in R4-1915520. WF for intra-band UL CA for FR1 power class 3 was approved in R4-1910273 – Objective completed
Rx requirement for NR intra-band contiguous CA was agreed in R4-1916015 – Objective completed
Tx switching between case 1 and case 2
  LS to RAN2 on UE capability and required RRC signaling was approved
  RRM: Requirements for Tx switching between two UL carriers: Initial discussion in RAN4 #93. RAN4 agreed to further study further study if interruption requirements shall be defined and the interruption length in RAN4 #94
SR completion level: 50% for core part, 20% for perf. Part

## Slide 10: FR2 UE RF
MPE: Based on RAN agreed timeline, RAN4 approve LS to RAN2 on required MAC-CE signalling to address MPE issues. RAN4 also did not see any needs for RAN1 spec changes. RAN4 will continue discuss the detailed solutions in Q1 2020.
Beam correspondence: WF for side condition for CSI-RS only and SSB only test are approved. WF for BC enhancement was approved
RAN4 also achieve some progress on the objectives including intra-band DL CA, intra-band non-continuous UL CA, inter-band DL CA, MPR enhancement and spherical coverage enhancement
RAN4 discussed inter-band uplink CA but no agreement reached. It is proposed to remove this objective from the WI.
SR completion level: 25% for core part, 25% for perf. Part

## Slide 11: RRM Requirements Enhancements
RRM
  RRM work started in Q4’19 (work plan approved in Q3’19)
  Good progress for SRS carrier switching, multiple SCell activation, CGI reading, BWP switching on multiple CCs, inter-frequency measurement without MG and mandatory gap patterns objectives with multiple agreements reached in Q4.
  No progress on non-simultaneous UL carrier operation in FR2, and FR2 Inter-band CA objectives due to dependency on the RF room progress.
RAN #86 proposals for updating the WI objectives
  RP-192882: Remove objectives “UE specific CBW change”, “Non-simultaneous UL carrier operation in FR2”. Update “Inter-band CA requirement for FR2” objectives based on RF session progress.
  RP-192666: Add objectives on TCI state switch of the CSI-RS for CSI reporting and spatial relation switch for uplink .
SR completion level: 40% for core part, 0% for perf. part.

## Slide 12: CSI-RS based L3 Measurement
RRM
  RRM Core work started in Q4’19 (work plan approved in Q3’19)
  Way forwards on CSI-RS based RRM measurements requirements were approved in R4-1910956 and R4-1913749.
  Link-level simulation assumptions for CSI-RS based measurements was approved in R4-1910949.
  CSI-RS based intra-frequency and inter-frequency measurement definition is FFS which has a big impact on the progress for several objectives. Candidate definition options identified and to be selected in RAN4 #94.
SR completion level: 30% for core part, 0% for perf. part.

## Slide 13: High Speed Train Scenarios
RRM
  WFs on RRM for NR HST were approved in R4-1912781, R4-1915887.
  Link-level simulation assumptions agreed in R4-1912841, R4-1912842
  LS on the UE capability and network assistance signaling was approved in R4-1915855
Demodulation
  Good progress on UE Demodulation. Agreed to define requirements for HST-SFN, HST single tap and fading conditions. Many simulation assumptions agreed.
  Good progress on BS Demodulation. Staged approach and prioritization for requirements definition agreed. Many simulation assumptions agreed.
  LS to RAN2 on the UE capability and network assistance signaling approved in R4-1915916.
  RAN4 will continue to study feasibility and performance benefits of additional transmission schemes in Q1’20.
SR completion level: 50% for core part, 45% for perf. part

## Slide 14: Performance requirement enhancement
Demodulation
  Good progress on both UE and BS Demodulation including UE CA normal demodulation, UE TDD LTE-NR co-existence, UE PMI reporting and BS PUSCH requirements
  UE CA power imbalance: Demod work put on hold in Q4’20 due to lack of RF requirements. WF on Rx image requirements agreed in RAN #93 and Demod work expected to resume in Q1’20.
  UE CA CQI requirements: work planned to start in Q1’20 in accordance to WID
RAN #86 proposals for updating the WI objectives
  RP-192532: Define UE CA CQI requirements for AWGN case only
SR completion level: 40% for perf. part

## Slide 15: FR2 DL 256QAM
RAN4 conclude the feasibility of FR2 DL 256QAM
BS TX EVM core requirement for DL 256QAM FR2 is agreed as 3.5%
SR completion level: 80% for Core part and 0% for perf. part

## Slide 16: NR – Other WG led items

## Slide 17: Rel-16 NR – eMIMO
RF
  WF for full power transmission test cases have been approved
  Simulation assumption for MPR evaluation for pi/2 BPSK DMRS has been approved
RRM
  RRM Core work started in Q4’19
  RRM requirement scope agreed in WF R4-1912742
  Details of NR eMIMO RRM requirement agreed in WF R4-1915850
  Reply to RAN1 LS on applicable timing for pathloss RS activated/updated by MAC-CE was approved (R4-1915929)
    SR completion level: 95% for core part, 0% for perf. part

## Slide 18: Rel-16 NR – CLI and RIM
RRM
  Reporting range for SRS-RSRP and CLI-RSSI were agreed and sent LS to RAN2
  CRs for CLI RRM Core requirements agreed
  All RRM Core requirements open issues were finalized.
  RRM Performance part will start in Q1’20.
SR completion level: RAN4 - 90% for core part, 0% for perf. part

## Slide 19: Rel-16 NR – NR-U
RF
  NR-U general SEM is agreed in R4-1915979
  WF and draft CRs for other system parameters including channel raster, sync raster, guard-band design were also approved
  Input from operators request on band combinations were collected. The WID is supposed to be updated by captured these band combination requests.
RRM
  Key agreements are captured in WFs R4-1915777, R4-1912851
  Outline specification structure for 36.133 and 38.133 NR-U requirements agreed
RAN #86 proposals
  RP-192775: Rapporteur’s views on the remaining open issues and timelines
SR completion level: RAN4 ~ [50]% for Core part

## Slide 20: Rel-16 NR – eURLLC
RRM
  RAN4 agreed not to introduce a mechanism to prevent RLF for URLLC in the scope of R16 NR eURLLC WI
  RRM Core/Performance work is finalized
Demodulation
  Good progress achieved on test feasibility for 10-5 BLER
    Key agreement captured in R4-1912725, R4-1915866
    In RAN4 #94 companies should present their evaluation of test time and their preferred methodology to conclude on test feasibility
  Initial scope on UE and BS demodulation requirements agreed in WF R4-1915913
    SR completion level: 95% for core part, 20% for perf. part

## Slide 21: Rel-16 NR – Power Saving
    RF
  No consensus reached on switching time for MIMO layer adaptation
    RRM
  Way forwards on RRM measurement relaxation for Power Saving were agreed (R4-1910948 and R4-1915946)
    SR completion level: 90% for core part, 0% for perf. part

## Slide 22: Rel-16 NR – Positioning
    RRM
  RRM Core work started in Q4’19 (only work plan approved in Q3’19)
  Skeleton for the TS 38.133 agreed
  System level simulation assumptions approved in R4-1912732.
  Ad-hoc minutes for NR Positioning RRM work were approved in R4-1912793
  RAN4 WG endorsed ad-hoc meeting minutes for NR Positioning RRM in R4-1915848 and agreed on a way-forward for NR Positioning R4-1915854
  Link level simulation assumption for PRS RSTD that were agreed in R4-1915802
  Reference Point for UE and gNB Timing Measurements agreed and LS to RAN1 was sent
  No final decision whether to define gNB RRM performance requirements in R16 timeframe
    SR completion level: 80% for core part, 0% for perf. part

## Slide 23: Rel-16 NR – 5G V2X and NR sidelink
    Several response LS to other WG were discussed in RAN4 and approved on
  AGC settling time for PSFCH
  NR V2X cross-RAT configuration
  Simultaneous transmission of PSFCH
  UL-SL prioritization
  Transient period for SSB design
    RF
  RAN4 agreed the V2X operation scenarios and prioritizations
  Several TPs on system parameters and RF requirements for both unlicensed band licensed bands were approved
    RRM
  WFs for NR V2X RRM requirements scope were approved in R4-1912708, R4-1915783
  Link-level simulation assumption agreed (R4-1912828)
  Initial Draft CRs were endorsed
    SR completion level: 85% for core part, 0% for perf. part

## Slide 24: Rel-16 NR – NR Mobility Enhancement
RRM
  Key agreements captured in WFs R4-1913436 and R4-1911041
  LS to RAN2 on NR Mobility Enhancements agreed in R4-1912707
  Reply LS to RAN2 on UE capabilities on DAPS HO agreed in R4-1915781
  Initial Draft CRs were endorsed
SR completion level: 70% for core part, 0% for perf. part

## Slide 25: Rel-16 NR – MR-DC
RRM
  WFs on MR-DC RRM requirements agreed in R4-1912717, R4-1915842
  Reply LS to RAN2 on direct SCell activation in RRC resume message was approved in R4-1915844
  Discussion on support of asynchronous and synchronous NR-NR DC is subject to RAN1 progress
    SR completion level: 95% for core part, 20% for perf. part

## Slide 26: Rel-16 NR – IAB
    General
  TS skeleton and skeleton was during e-mail discussion which is supposed to be approved before Feb meeting
    RF
  A set of agreements for RF requirements for both IAB MT and IAB DU
    RRM
  RRM Core work started in Q4’19
  T_delta for IAB OTA timing alignment agreed and LS to RAN1 approved (R4-1912714)
  RAN4 spend substantial efforts to agree on a set of IAB RRM requirements to be defined in Rel-16 timeframe.
  Limited progress with details of the exact RRM requirements.
RAN #86 proposals
  RP-192949: propose to define additional “RLM and BFD/BFR requirements for the MT”
    SR completion level: RAN4 - 40% for core part, 0% for perf. part

## Slide 27: Rel-16 NR – SRVCC from 5G to 3G
RRM requirements were finalized
CRs to TS 38.133 were agreed
SR completion level: 95% for core part, 0% for perf. part

## Slide 28: Rel-16 NR –Spectrum WI(1/2)
Completed items are summarized in slide 7
Band n26
  Emission requirements and REFSENS were agreed
Band n259
  WF for UE and BS RF requirements were approved
  No consensus on the multi-band relaxation
Addition of channel BW in NR band n1 (NR_n1_BW & NR_n1_BW2)
  50MHz is proposed to be added in NR_n1_BW2 WI
Addition of wider channel bandwidths in NR band n28
  BS-BS co-existence, UE spurious emission, Delta MPR for 30MHz
29 dBm UE Power Class for LTE band 41 and NR Band n41
  RAN4 approved the WF on power class and tolerance requirements in R4-1916179
  RAN4 discussed regulatory requirements and A-MPR improvement. No agreements yet.

## Slide 29: Rel-16 NR –Spectrum WI(2/2)
  Addition of asymmetric channel bandwidth for NR band n66
  WF on support of asymmetric channel bandwidth for n66 was approved in R4-191618
  Introduction of NR FDD bands with variable duplex
  It is identified that timing mask requirement shall be defined as generic requirements for all the bands including New FDD bandwih variable duplex and other bands with uplink sharing
  RAN4 chairman proposed to define the generic requirements in separate WIs and close WI with band specific requirements
  RAN4 has technically endorsed CRs to 38.104 and 38.141-1
  Companies submit the company CRs to RAN #86 to close the WIs
  Action to RAN
    RAN guideline on which WI to capture generic requirements of timing mask is needed. Based on guideline, RAN decision on handling company CRs and also completion of WI is needed

## Slide 30: Rel-16 Basket WI Status
Rel-16 NR Basket WI Status Report
Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
NR intra-band CA | RP-192441 | RP-192445
NR Inter-band CA for 3 bands DL with 1 band UL | RP-192869 | RP-192868
NR Inter-band CA for 4 bands DL with 1 band UL | RP-192443 | RP-192447
EN-DC for 2 bands DL with 2 bands UL (1 LTE band + 1 NR band) | RP-192741 | RP-192742
EN-DC for 3 bands DL with 2 bands UL (2 LTE bands + 1 NR band) | RP-192814 | RP-192815
EN-DC for 4 bands DL with 2 bands UL (3 LTE bands + 1 NR band) | RP-192442 | RP-192446
EN-DC for 5 bands DL with 2 bands UL (4 LTE bands + 1 NR band) | RP-192767 | RP-192768
EN-DC for 6 bands DL with 2 bands UL (5 LTE bands + 1 NR band) | RP-192779 | N/A
EN-DC of x bands (xDL/1UL x=1.2,3,4) LTE and 2 NR bands (2DL/1UL); | RP-192593 | R4-192592
EN-DC for 3 bands DL with 3 bands UL | RP-192538 | RP-192537
NR Inter-band CA/DC for 2 bands DL with up to 2 bands UL | RP-192614 | RP-192615
NR Inter-band CA/DC for 3 bands DL with 2 bands UL | RP-192616 | RP-192617

## Slide 31: Rel-16 NR – SI
7-24 GHz
  Several TPs for system parameters, BS RF and UE RF were approved
MIMO OTA
  RAN4 concluded all the open issues, including the test metrics and test methods, for FR1
  RAN4 also achieve the progress on test methods for FR2 and further extension (1 quarter) is needed to complete the FR2 test methods
High power for EN-DC (FDD + TDD)
  SI completed and WI proposal in RP-192830
FR2 Test enhancement
  Workplan and TR skeleton were approved
  RAN4 only focus on objective 1, 2 and 3 in Q4.

## Slide 32: LTE

## Slide 33: Rel-16 LTE
eMTC5
  RRM: Good progress on RRM requirements finalization. WFs agreed in R4-1912735 and R4-1915889.
  Demodulation: A work plan was agreed in R4-1914344, and a WF agreed in R4-1915876.
  SR completion level: 90% for core part, 10% for perf. part
NB-IOTenh3
  RF: TP on summary of co-existence study and power boosting requirements were approved
  Conformance testing: WF for test cases for NR in-band operation was approved
  RRM: Good progress on RRM requirements finalization. WFs agreed in R4-1912783 and R4-1915890.
  Demodulation: a WF was agreed in R4-1915909.
  SR completion level: 90% for core part, 10% for perf. part

## Slide 34: Rel-16 LTE
LTE MIMO
  RAN4 agreed response LS on UE capability of guard period for SRS with frequency hopping and antenna switching
Even further mobility enhancement
  RRM: WFs on RRM requirements agreed in R4-1912784 and R4-1915920
  Initial CRs agreed
  SR completion level: 75% for core part, 10% for perf. part
LTE high speed
  RRM: requirements finalized, CRs agreed
  Demodulation: UE Demodulation requirements finalized. BS Demodulation requirements need another round of alignment for PUSCH.
  SR completion level: 100% for core part, 95% for perf. Part
  1Q extension requested by rapporteur
LTE-based 5G terrestrial broadcast
  Work plan agreed in R4-1911284
  RRM: WF and CRs for RRM requirements agreed
  SR completion level: 95% for core part, 0% for perf. Part

## Slide 35: Rel-16 LTE Spectrum related WI
Rel-16 LTE Basket WI Status Report
  Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
LTE intra-band CA | RP-192440 | RP-192444
LTE inter-band CA for 2 bands DL with 1 band UL | RP-192524 | RP-192525
LTE inter-band CA for 3 bands DL with 1 band UL | RP-192810 | RP-192811
LTE inter-band CA for x bands DL (x=4, 5) with 1 band UL | RP-192424 | RP-192423
LTE inter-band CA for 2 bands DL with 2 band UL | RP-192812 | RP-192813
LTE inter-band Carrier Aggregation for x bands DL with 2 bands UL | RP-192587 | RP-192686
Additional LTE bands for UE category M1 and/or NB1 | RP-192455 | RP-192453
Additional LTE bands for UE category M2 and/or NB2 | RP-192456 | RP-192454

## Slide 36: New Rel-16 Proposals

## Slide 37: New WI/SI proposals
  Spectrum related proposal for NR (6)
  WI: New WID: Dual Connectivity (EN-DC) of LTE inter-band CA xDL/1UL bands (x=2,3,4) and NR FR1 1DL/1UL band and NR FR2 1DL/1UL band
  WI: Power Class 2 UE for EN-DC (1 LTE FDD band +1 NR TDD band)
  WI: New basket WID: adding new channel bandwidth(s) support to existing NR bands
  WI: Adding 40 MHz channel bandwidth (15, 30 and 60kHz SCS) in NR band n3
  WI: Adding 50 MHz channel bandwidth (15, 30 and 60kHz SCS) in NR band n65
  WI: Introduction of NR Band n53
Spectrum related proposal for LTE (0)
Non-Spectrum related proposals for NR (0)
Non-Spectrum related proposals for LTE (1)
  WI: introduction of NB-IoT in AAS specification

## Slide 38: New Rel-17 Proposals

## Slide 39: New WI/SI proposals
  Spectrum related proposal for NR (2)
  WI: introduction of brand new channel bandwidths for NR
  WI: Spectrum sharing between NR and LTE refarming band
Spectrum related proposal for LTE (1)
  SI: high-power UE operation for fixed-wireless/vehicle-mounted use cases in Band 12 and in Band 5
Non-Spectrum related proposals for NR (4)
  WI: 1024 QAM for NR FR1
  WI: RLM requirement enhancement for VoNR
  WI: PC5 for FR2
  WI: measurement gap enhancements
Non-Spectrum related proposals for LTE (1)
  WI: supporting overlapping CA for LTE
    Based on RAN #84 guideline (RP-191551), RAN4 R17 proposals will be discussed and decided in RAN #87
    Based on the workload estimation, it is suggested not to start Rel-17 items in RAN4 before Q3 2020

## Slide 40: Thanks to
  NR specifications rapporteturs and their companies for their extraordinary effort of coordinating the RAN4 discussions and also editing RAN4 NR specifications:
  Ville Vintola (Qualcomm): 38.101-1/2/3
  Johan Sköld (Ericsson): 38.104
  Yang Tang (Intel): 38.133
  Haijie Qiu (Samsung): 38.101-4
  Steven Chen (Huawei): 38.141-1/2
  Aijun Cao and Rui Zhou (ZTE): 38.113
  Christian Bergljung (Ericsson): 38.124
  Petri Vasenkari (Nokia): 38.307
  Kyoungseok Oh and Kai-Erik Sunell for efficient secretary support
  AH chairs and WI rapporteurs for coordinating the offline/ad-hoc discussions
  Delegates for enthusiastic contributions
  CF3 and NF3 for meeting hosting

## Slide 41: Special thanks to all RAN4 delegates for your kindly and always support in my last 4 years term