## Slide 1
Views on Rel-17 RP-192404 IITH, Reliance Jio, IITM, CEWIT, Tejas Networks

## Slide 2
pi/2 BPSK feature in Rel-15 and Rel-16
Fix the loopholes in the pi/2 BPSK feature in the 3GPp Rel-15 and Rel-16 specifications
Currently filtering/ spectrum shaping is spec transparent
Spec doesn’t clearly explain how filtering must be done for multiple port PUSCH transmissions
  Else the spec is broken
RP-192403 has more details
Status of email discussion: Not considered in “coverage” or “MIMO” items

## Slide 3
Coverage extension
LMLC requirements i.e., meeting low-mobility with large cell radius such as 12 Km ISD and beyond must be achieved
  all the DL and UL physical channel be able to operate at very low SNR, eg -14 dB.
  Low SNR operation not only improves rural coverage, the benefit extends to urban scenarios where high wall penetration losses are encountered
The current specifications do not always guarantee such low SNR operation in DL and UL
Significant improvement of physical channel operation is possible
  e.g., Beam sweeping in sub-6GHz provides the additional coverage compared to fixed sector scenario.
Proposal: Study the link level performance of all DL and UL physical channel operation to attain low SNR operation.
  Identity the "weak" links and specify necessary enhancements to improve low SNR operation
  Target data rate of at least 512 Kbps for Rural scenario
Status: ISD and target data rates and target system SNR operation yet to be agreed

## Slide 4
MIMO
MIMO Enhancements
Non-linear precoding: its impacts on data channels and reference signals must be studied. This will significantly enhance NR SE.
Study the impact of TDD/FDD reciprocity in improving MIMO/beamforming performance
Reciprocity based MIMO enhancements for carrier aggregation
High Speed UE and Train Scenarios
Enhance the DL reference signals and UL reference signals (CP-OFDM and DFT-s-OFDM) for high speed scenarios with speeds up to 500 kmph, e.g. PTRS density enhancement for sub-6 GHz
CSI enhancement such as explicit interference measurement, doppler compensation
Enhanced Interference Measurement and Feedback
Interference measurement and feedback be improved in NR for enhancing the performance of MU-MIMO. Explicit feedback and feedback compression techniques can be explored as part of this study.
The channel will remain nearly static for fixed and low speed scenario. However, the interference can vary due to various factors like MU-MIMO, scheduling of resources in adjacent gNB, etc. Explore the possibility of interference only feedback report for the above case.
SRS enhancements
SRS triggering enhancements to improve coverage and throughput
Status: Our inputs not yet captured in the WID draft

## Slide 5
Flexible UL DL resource utilization
Signaling framework for flexible UL DL resource utilization
Study whether existing signaling framework is enough for dynamic resource utilization for multi-TRP with same cell ID scenario
Study enhancements related to semi static UL DL resource utilization
Intra-cell cross-link interference (CLI) management
Framework for intra-cell CLI measurement and management
Study whether existing signaling techniques are enough to manage intra-cell CLI
Enhancement to CLI measurement and reporting techniques
Introduce L1 based CLI measurement and reporting to support dynamic UL DL resource utilization
SRS configuration sharing among gNBs/TRPs for accurate RSRP measurement
Study any other feature as a part of enhancement to CLI management which was not discussed in Rel.16 due to lack of time

## Slide 6
Positioning Enhancement
Enhancement in UE based positioning For Rel 17
Same accuracy and reliability for deep indoor scenario compared with other cases in Rel 16.
Enhanced privacy and security.
Power optimization especially for IoT devices
UE’s with good coverage/in-coverage can assist UE’s in partial coverage
Support V2X, IIoT and high mobile usecases
Support for positioning in inactive and idle mode in Rel 17
It is beneficial for overhead reduction, power consumption reduction and latency reduction.
Enhanced privacy and security.
Support for NavIC in NR and E-UTRA
NavIC WID is agreed in Rel 16 for LTE. Its support needs to be extended further for other RAT in Rel 17.
Enhance the A-GNSS support for NB-IoT
Battery optimization with respect to UE A-GNSS for NB-IoT should be standardized

## Slide 7: IAB enhancements
Resource allocation between backhaul and access links
    FDM, SDM and Full duplexing techniques
Power control enhancements
    To handle Tx from child IAB to parent that overwhelm access UE Tx
Self interference and cross interference mitigation
Timing alignment between backhaul and access links
    Study of Case #6 and Case #7 timing
Signaling support for FDM/SDM/Full duplex schemes