## Slide 1: LG view on Rel-17 NR above 52.6GHz
3GPP TSG RAN Meeting #86
Sitges, Spain, December 9-12, 2019
RP-192765
Source: LG Electronics
Document for: Discussion
Agenda Item: 9.1.1

## Slide 2: 1. Introduction
NR above 52.6GHz SI has been discussed via RAN email reflector as one of the Rel-17 candidate items.
NR above 52.6GHz SI has large uncertainties
  in the potential scope of work
  In the potential procedure of handling large frequency spectrum, e.g. 52.6GHz ~ [114.25]GHz
In the email discussion, 2-phase SI approach was suggested such as
  1st phase includes study for 52.6GHz ~ 71GHz
  2nd phase includes study for 71GHz~[114.25]GHz

## Slide 3: 2. Discussion
NR above 52.6GHz SI should include waveform study and study on the relevant numerologies rather than including all the specification impacts to design a system
If 2-phase approach is introduced, the purpose and the practical feasibility under the Rel-17 timeline should be carefully discussed, including
  whether the target is licensed band or unlicensed band or both
  whether the target is to enable and complete WI during Rel-17
  Practical feasibility of completion of the potential WI under Rel-17 timeline

## Slide 4: 3. Proposal
NR above 52.6GHz SI should include
  Study on the waveform over 52.6GHz ~ [114.25]GHz
  Study on the numerologies and the basic frame structure if necessary for the waveform/numerology discussion
For the study procedure, following two options should be discussed on the basis of clear purpose and benefits
  Option 1) Single phase Rel-17 SI
    waveform (and corresponding numerology) study for 52.6~[114.25]GHz
  Option 2) 2-phase Rel-17 SI
    1st phase: waveform (and corresponding numerology) study for 52.6GHz~71GHz
    2nd phase: waveform (and corresponding numerology) study for 71GHz~[114.25]GHz

## Slide 5: 3. Proposal
For option 2, the following details should be discussed
  1st phase: waveform (and corresponding numerology) study for 52.6GHz~71GHz
    option 2-1) evaluation assumptions, KPIs for 52.6GHz~[114.25]GHz
    option 2-2) evaluation assumptions, KPIs for 52.6GHz~71GHz
    If it is concluded that specification impact for 52.6GHz~71GHz is marginal and can be completed within Rel-17 framework, a WI for 52.6GHz~71GHz can be considered during Rel-17
      option 2-x-1) targeting Rel-17 WI for licensed band only
      option 2-x-2) targeting Rel-17 WI for both licensed band and unlicensed band
  2nd phase: waveform (and corresponding numerology) study for 71GHz~[114.25]GHz
    targeting WI for ~[114.25]GHz in Rel-18
In any option, it is desirable to target unified waveform design over 52.6~[114.25]GHz unless very strong necessity of differentiation of waveform is justified by the study
In case of option 2), if it is intended to open a WI for Rel-17 for 52.6GHz~71GHz in Rel-17 timeline, Rel-17 WI scope should be minimized.