## Slide 1: Views on Power Saving in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #86 RP-192856
Sitges, Spain, December 9th -12th , 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: NR Evolution to Rel-17 and Beyond
User-oriented system evolution –
  Better user experience is one important aspects in marketing NR and further development
  NR power consumption is more than double of that in LTE
    NR PDCCH monitoring in CONNECTED mode is more than double of that in LTE
    Initial access power is more than double of that in LTE
  Power consumption is high in EN-DC due to individual configuration of DRX for LTE and NR
Green project – reduce power consumptions to protect the earth
Rel-16 power Saving study and works provide the framework for UE power saving for eMBB
  Continue power consumption reduction at UE and gNB
Power savings for other Rel-17 SIs/WIs
Coordination among power saving for some Rel-17 features
  Rel-17 NR Light
  Rel-17 eV2X
  Rel-17 Positioning enhancement
  Rel-17 AR/VR
  Rel-17 NB-IoT/eMTC enhancement
  Rel-17 Broadcast

## Slide 4: UE Power Saving Study in Rel-16
Rel-16 Study on UE power saving gains had been shown in multiple dimensions
  UE adaptation to the DRX operations in RRC_CONNECTED mode
    Power saving signal/channel in triggering UE adaptation
    Dynamic DRX configuration
  Reduce PDCCH monitoring
    PDCCH skipping
    Switching PDCCH monitoring periodicity
    Blind decoding reduction
  UE adaptation to the BWP/SCell operation
  UE adaptation to the maximum number of MIMO layers/ number of antenna
  UE assistance information
  RRM measurements reduction
    Relaxing in time domain
    Relaxing in intra and inter-frequency measurements
    Measurements with Additional RS
UE assistance for fast transition from RRC_CONNECTED to RRC_IDLE/RRC_Inactive

## Slide 5: UE Power Saving Work in Rel-16
Specify power saving techniques with PDCCH-based power saving signal/channel triggering UE adaptation in RRC_CONNECTED mode [RAN1, RAN2, RAN4]
  Specify procedures triggering a MAC entity to “wake up” to monitor PDCCH at reception of the PDCCH-based power saving signal/channel for the next occurrence(s) of the drx-onDurationTimer [RAN2, RAN1]
    NOTE: Any change of PDCCH channel coding and payload interleaver is not in the scope
  Specify the procedure of cross-slot scheduling power saving techniques [RAN1, RAN4]
    NOTE: The procedure is in addition to Rel-15 cross-slot scheduling procedure
Specify the power saving techniques of UE adaptation to the maximum number of MIMO layers [RAN1, RAN2, RAN4]
  Specify configuration of a different MIMO layer configuration of the initial/default BWP compared with other BWPs of a Serving Cell. [RAN2, RAN4]
    Discuss whether to also extend this to define per-BWP MIMO layer configuration [RAN1, RAN2]
  Evaluate if switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers are needed and which case assuming a relationship between the number of RF ports and the MIMO layer configuration [RAN4]
    NOTE: Switching on/off the RF is part of the evaluation
Specify a mechanism for a UE to indicate its preference of transitioning out of RRC_CONNECTED state. [RAN2]
Specify, if agreed, the mechanism to provide UE assistance information [RAN2, RAN1]:
Study and select among the following UE assistance information for RAN2 by RAN#85:
power preferred information (baseline LTE PPI in a well-defined manner) and UE's preference on C-DRX, BWP and SCell configuration [RAN2].
  NOTE: additional UE assistance information for RAN1-specific power saving techniques to indicate what setting of parameters related to this Work Item will lead to power savings for the UE can be included if agreed in RAN1.
Specify network-configured mechanism to relax intra and inter-frequency RRM measurement for neighbour cells for RRC_IDLE/INACTIVE with minimal mobility performance impacts [RAN2, RAN4]
  Specify RRM measurement relaxation by allowing measurements with longer intervals, and/or by reducing the number of cells/carriers to be measured [RAN4, RAN2]
  Define triggering criteria for the UE to move between relaxed and normal RRM measurements, that considers at least if UE is not at cell edge, or if UE is stationary or with low mobility [RAN2, RAN4].
    Evaluate and specify requirements (if needed) depending on RAN2 criteria [ RAN4]
    NOTE: No new measurement quantities should be introduced

## Slide 6: Power Saving Scope in Rel-17
Multi-RAT UE power saving in CONNECTED and IDLE mode
  IDLE mode enhancement in multi-RAT – low power consumption power saving signal/channel to trigger UE monitoring paging occasion and system information
  Temperate RS in assisting UE channel tracking and measurements in IDLE mode for power consumption reduction
PDCCH monitoring reduction
  PCell /SpCell PDCCH monitoring reduction – PDCCH skipping
    Support of small data power consumption in CONNECTED mode
  Further SCell PDCCH monitoring reduction
    PDCCH monitoring reduction for SCell in non-dormancy like behavior, in particular for SCell with large SCS in FR2
Power saving techniques for Rel-17 enhanced beam management in FR2
  Power saving for FR2 beam measurements - temperate RS
  Power saving for FR2 beam reporting