## Slide 1: Views on NR-Light in Rel-17
CATT
RP-192859
3GPP TSG RAN WG Meeting #86
Sitges, Spain, Dec. 9-12, 2019
Document for: Discussion
Agenda Item: 9.1.1

## Slide 2: General views on NR light
An SI or a study phase is necessary to:
  determine the number of UE RX/TX antennas and UE bandwidth to satisfy the target use cases while achieving reasonable UE cost/complexity reduction
  study to what extent the UE power class can be reduced considering tradeoff between benefit of UE complexity/form factor reduction and coverage loss
  study necessity of other UE complexity reduction techniques and identify the required specification efforts if the technique is agreed
Specify the techniques based on the outcome of SI/study phase, and ensure the techniques are applied to intended UE types
Proposal: An SI or a study phase is necessary to establish a clearer WI scope.

## Slide 3: Overlapping with other Rel-17 items
NR light has potential overlapping with the following Rel-17 items
  UE power saving
    The potential UE power saving schemes targeting for NR light UEs are also beneficial for and can be applied to “normal” UE types
  Coverage enhancements
    Unified solutions for coverage enhancements are desired although the targets for NR light and coverage enhancements may be different
  Small data enhancements
    There is commonality in terms of large number of UEs and small packet transmission
Proposal: UE power saving, coverage enhancements and small data enhancements targeting for all UE types are included in respective UE power saving, coverage enhancements and small data enhancements items in order to avoid duplicate discussions in different items and to strive for unified solutions.