## Slide 1: Views on NR Positioning in Rel-17
RP-192860
3GPP TSG RAN WG Meeting #86
Sitges, Spain, December 9-12, 2019
Document for: Discussion
Agenda Item: 9.1.1
China Academy of Telecommunications Technology (CATT)

## Slide 2
Rel-16 NR Positioning SI (completed in RAN#83)
  Defined target regulatory and commercial performance requirements for Rel-16
  Defined three NR positioning evaluation scenarios (Indoor office, UMi, UMa) for system level analysis
  Concluded that it is feasible to achieve the target regulatory and commercial performance requirements for horizontal positioning accuracy for the evaluation scenarios
Rel-16 NR Positioning WI (to be completed in RAN#87)
  Focuses on the RAT-dependent positioning techniques recommended by Rel-16 NR Positioning SI, namely, DL-TDOA, DL-AoD, UL-TDOA, UL-AoA, RTT and E-CID
  GNSS SSR (PPP-RTK support) based on the “Compact SSR” definitions specified for QZSS
  DL-only UE based positioning
R16 NR Positioning SI/WI

## Slide 3
Motivations of R17 NR Positioning Enhancements
5G positioning performance requirements [TS 22.261, TS 22.104]
Absolute positioning
  Horizontal: accuracy 10m to 0.3m with 95% confidence and 95% to 99.9% availability
  Vertical: 3m to 2m with 95% confidence and 95% to 99.9% availability
Relative positioning
  Horizontal: 0.2m with 95% confidence and 99% confidenceVertical: 0.2m with 95% confidence and 99% confidence
Time latency (time to first fix): from seconds to ms
  Target Rel-16 positioning performance (TR 38.855)
  Horizontal positioning error < 3m (80%) (indoor ) and < 10m (80%) (outdoor)
  Vertical positioning error < 3m (80) (indoor) and error < 3m (80) (outdoor)
  Time latency (time to first fix) < 1 second
Significant gap between R16 target positioning performance [TR 38.855] and 5G positioning performance requirements [TS 22.261, TS 22.104] in terms of positioning accuracy, latency, availability, and reliability.

## Slide 4
5G NR needs to support much more use cases of 2D/3D positioning with high accuracy, low latency and high reliability, e.g.,
  Idle and inactive UEs
  V2X positioning
  IoT positioning
Many promising techniques were actually proposed during Rel-16 NR Positioning SI/WI but were not further investigated in Rel-16, e.g.,
  NR carrier phase based positioning
  Multipath mitigation techniques, such as LOS detection, multiple measurements reporting
  Corporative positioning
  Differential NR positioning
  Precise time/phase and frequency synchronization of the wireless network based on NR reference signals
  …
Motivations of R17 NR Positioning Enhancements

## Slide 5
Carrier phase positioning (CPP) is commonly in GNSS for cm-level positioning (e.g., RTK, PPP). CPP technique can also be used in NR for cm-level positioning based on NR PRS and/or NR carrier-PRS.
NR has a number of salient advantages over GNSS in CPP
  Has much higher receiving signal power
    Quicker phase-lock
  Allow flexible configuration for the transmission of reference signals
    Faster integer ambiguity resolution
    Better RF resource Optimization
    Lower implementation complexity
  Work in any environment where NR reference signal can be reliably detected, including the locations where GNSS signals are not available
NR carrier phase positioning

## Slide 6
High-accuracy positioning (with the velocity and heading) with very low latency are critical for V2X operation
Using multiple antennas, MIMO and large carrier bandwidth will increase AOA and TOA measurement accuracy and reliability for V2X positioning
Carrier phase positioning (GNSS CPP and/or NR CPP) can also be used together with other techniques (e.g., IMU) to support high-performance V2X positioning.
Cooperative positioning with the information exchange among UEs can improve V2X positioning performance
High-Accuracy Positioning for V2X
Vehicle B
Vehicle B
x
y
Vehicle A
A1
A2
B1
B2
Information Exchange

## Slide 7
Differential techniques are commonly used in GNSS positioning
  increase the positioning accuracy by one order of magnitude or more
Differential positioning can also be applied in NR positioning
  One (or more) receiver at a known location is used as the reference receiver
  The receiver estimates the error corrections for the neighboring TRPs
    e.g., RSTD errors caused by TRP time misalignment
  Estimated error correction are used by the location server or the UEs to eliminate the measurement errors for high-accuracy positioning
Differential NR Positioning
TRP 1
Reference
Receiver
TRP 2
TRP 2
Differential corrections
LMF
UE

## Slide 8
Specify the solutions for high accuracy positioning based on A-BDS
  B1C signal is introduced in Rel-16 for A-BDS positioning
  Satellite signals from multiple carrier frequencies are commonly used in GNSS positioning for improving the system performance
  B2a signal should be introduced in Rel-17 for high-accuracy A-BDS positioning
  LPP protocol needs to be extended to support multiple frequencies positioning with B2a signal for A-BDS for both LTE and NR
High accuracy A-BDS positioning