## Slide 1: Motivation for Study on RF requirements for NR FR1 frequency range 6.425-7.125GHz
Ericsson
RP-200308
3GPP TSG-RAN Meeting #87e
Electronic meeting, March 16-19, 2020
Agenda item: 9.1.1

## Slide 2: Motivation – ITU-R WP5D
ITU-R WP5D sent LS (RP-200042) to RAN asking for technical parameters for compatibilities studies in preparation of WRC-23 in following frequency ranges:
  470-694 MHz, 694-960 MHz, 1 710–1 885 MHz, 1 885-1 980 MHz, 2 010-2 025 MHz, 2 110‑2 170 MHz, 2 500-2 690 MHz, 3 300-3 400 MHz, 3 600-3 800 MHz, 4 800‑4 990 MHz, 6 425-7 025 MHz, 7 025-7 125 MHz and 10.0-10.5 GHz.

## Slide 3: Motivation
There are existing LTE or NR bands covering frequency ranges from 470 MHz (band 31) up to 4990 MHz (band n79).
  No need to further study following frequency ranges, limits specified in TS 36.104/ TS 38.104 and TS 36.101 / 38.101-1 could be used:
    470-694 MHz, 694-960 MHz, 1 710–1 885 MHz, 1 885-1 980 MHz, 2 010-2 025 MHz, 2 110‑2 170 MHz, 2 500-2 690 MHz, 3 300-3 400 MHz, 3 600-3 800 MHz, 4 800‑4 990 MHz
  A first LS could already be sent to ITU-R WP5D with limits for those ranges.
The SI on 7-24 GHz used 10 GHz as an example frequency:
  Further discussion would be needed to define limits and reply to ITU-R LS on the 10.0-10.5 GHz frequency range, but a SI might not be required for this.

## Slide 4: Motivation – FR1 extension
FR1 range was extended from 6 GHz up to 7.125 GHz in Feb. 2019, but with the following agreement (RAN4#90b - Way Forward R4-1902221):
Core requirement in TS38.104, TS38.101-1 and TS38.101-3
  FR1 extension has no impact on RF requirements for existing NR bands in Rel-15
  For operation in the range of 410-450MHz and/or 6-7.125GHz , limits and applicability of core requirements shall be determined in the corresponding WI in Rel-16 or future release (Note).
Conformance requirement in TS38.141-1 and TS38.141-2
  FR1 extension has no impact on conformance testing requirements for existing NR bands in Rel-15 including MU and TT.
  For operation in the range of 410-450MHz and/or 6-7.125GHz , limits and applicability of conformance requirements shall be determined in the corresponding WI in Rel-16 or future release (Note).
Note: Bands in the range of 410-450MHz and/or 6-7.125GHz defined in a later release can still be implemented in Rel’15 products

## Slide 5: Motivation – 6GHz SI
Frequency ranges 6 425-7 025 MHz and 7 025-7 125 MHz shall be studied, assessing current FR1 limits:
  ACLR, REFSENS (SNR) and other related Rx requirements should be re-visited before answering ITU-R LS.
Proposed scope of this SI is limited to 6GHz study to optimize leadtime:
  ITU-R has tough deadline and expect 3GPP feedback as soon as possible.
    First meeting: June 2020.
    Deadline to collect latest inputs: February 2021.
  3GPP e-meetings might not always be efficient to progress on such study.

## Slide 6: Background: Expected parameters

## Slide 7: Background: Expected parameters

## Slide 8: Background: Expected parameters