3GPP TSG-RAN4 WG Meeting # 88-e	       RP-20xxxx

# Electronic Meeting, June 29 - July 3, 2020

Title:	draft LS on introducing UE capability for power class for NR band in MR-DC combination

Response to:

Release:	Release 16

Work Item:	TEI16

Source:	3GPP TSG RAN

To:	RAN2

Cc:	RAN4

Contact Person:

#### Name:	Liu Ye

E-mail Address:	leo.liuye@huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

1. Overall Description:

RAN4 has discussed an ambiguity that may arise in regard to the output power available on individual carriers when the UE is configured with an MR-DC configuration. Depending on UE implementation, in some circumstances a UE reporting PC2 for the MR-DC band combination may provide PC2 in each band, whereas in other cases the UE would provide PC2 for the band combination but PC3 in the NR band. Since currently only the PC2 for the band combination and PC2 for the standalone NR band can be signalled, it is ambiguous to the network whether PC2 or PC3 is applicable in the NR band in the MR-DC combination. To resolve this, RAN#88e agreed that a new per-BC power class capability signalling for Rel-16 should be introduced in addition to the existing MR-DC power class.

RAN respectfully requests RAN2 to develop new power class UE capability signalling applicable per-BC for NR band combination in an MR-DC configuration. This is in addition to the MR-DC power class, i.e. indicates that UE supports the newly indicated power class for the NR band also in addition the indicated power class for the MR-DC band combination.  The value range for the signalled power class values is { pc2, pc3, pc5 }.

2. Actions:

To: 3GPP TSG RAN WG2.

ACTION: RAN respectfully asks RAN2 to introduce the new per-BC capability signalling for Rel-16 according to the above-mentioned RAN decisions.

3. Date of Next TSG-RAN Meeting:

TSG RAN4 Meeting #89		14th – 17th September 2020		                 Electronic meeting

# Comments

The ambiguity is that the network does not know which case applies.