3GPP TSG-RAN4 WG Meeting # 88-e	       RP-20xxxx

# Electronic Meeting, June 29 - July 3, 2020

Title:	draft LS on introducing UE capability for power class for NR band in MR-DC combination

Response to:

Release:	Release 16

Work Item:	TEI16

Source:	3GPP TSG RAN

To:	RAN2

Cc:	RAN4

Contact Person:

#### Name:	Liu Ye

E-mail Address:	leo.liuye@huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

1. Overall Description:

An ambiguity can arise in regard to the output power available on individual carriers when the UE is configured with an MR-DC configuration. More details are provided in R4-2000063 [1].

RAN4 kindly requests RAN2 to develop signalling that adds to the existing signalling and provides an indication of the power class applicable for NR CA band combination in an MR-DC configuration. (This new per BC power class signalling on each carrier will apply in addition to the MR-DC power class). The signalling is likely to be similar to the ue-CA-PowerClass-N as defined for E-UTRA.

2. Actions:

To: 3GPP TSG RAN WG2.

ACTION: RAN respectfully asks RAN2 to introduce the new capability according to the RAN decision.

3. Date of Next TSG-RAN Meeting:

TSG RAN4 Meeting #89		14th – 17th September 2020		                 Electronic meeting

Reference

[1] R4-2000063， Clarification of Power Class related features， NTT DOCOMO, INC.