3GPP TSG RAN Meeting #88e	RP-20841

Electronic Meeting, June 29 - July 3, 2020

Source:	Qualcomm Incorporated (Rapporteur)

Title:	Rel-16 Work Item Exception for NR_IAB

Document for:	Approval

Agenda Item:	9.3.11

3GPP™ Work Item Exception

# Title : 	Integrated Access and Backhaul for NR

## Acronym  : 	NR_IAB

## Unique Identifier :	820070

Release 16 Submission form

| Feature / Item: |  |
| --- | --- |
| Affects: | UICC apps: | ME: | AN: | CN: | Others (specify): |
| Expected Completion Date: | RAN#89 (Sep. 2020) |
| Service(s) impacted: | None |
| Specification(s) affected: | TS 38.174, TR 38.809 |
| Task(s) within work which are not complete: | IAB-MT Features Finalize the list of IAB-MT features RAN4 RF core requirement: IAB-MT Tx power Maximum output power for LA IAB-MT type 1-H IAB-MT output power dynamics Side condition for the dynamic range definition Power control for LA IAB-MT Finalization of Pcmax,f,c IAB-MT Tx signal quality Definition of IBE(whether to define or not is still FFS) IAB-MT Unwanted emissions FR1 LA IAB-MT ACLR FR1 and FR2 LA IAB-MT OBUE FR1 and FR2 boundary between in-band and spurious region for LA IAB-MT Absolute ACLR(whether to define or not is still FFS) Tx spurious emissions for LA IAB-MT Emission scaling factor for IAB-MT type 1-O IAB-MT Reference Sensitivity FR1 OTA sensitivity for IAB-MT type 1-H and 1-O FRCs to be used for sensitivity definition/test IAB-MT Receiver Dynamic Range FR1 IAB-MT Rx dynamic range (whether to define or not is still FFS) In-band selectivity and blocking Bandwidth and offset of interfering signal for ACS and IBB of FR1 WA IAB-MT Type 1-H, 1-O ACS for FR1 LA IAB-MT type 1-H, 1-O IBB of FR1 LA IAB-MT type 1-H,1-O Receiver intermodulation Definition of Rx IM for FR1 IAB-MT(whether to define this or not is FFS) RAN4 RRM core requirement: Remaining issue on RLM evaluation period for IAB-MTs: FFS the relaxation factor of SSB and CSI-RS based RLM evaluation period in FR2 |
| Consequences if not included in Release 16: | RF requirements are not finalized and IAB nodes cannot be deployed Potential RLM requirement for IAB-MTs will not be completed in FR2 |

Abstract of document:

Contentious Issues: