## Slide 1
3GPP TSG RAN Meeting #89e RP-201636
Electronic Meeting, September 14 - 18, 2020
Agenda Item: 9.7.5
Source: Xiaomi
Title: Clarification on the understanding of peak data rate for wearable in Redcap
Document for: Discussion and decision

## Slide 2: Background#1
In the revised SID on study on support of reduced capability NR devices (RP-201386), the requirements for wearables are illustrated as follow
Wearables: Reference bitrate for smart wearable application can be 5-50 Mbps in DL and 2-5 Mbps in UL and peak bit rate of the device higher, up to 150 Mbps for downlink and up to 50 Mbps for uplink. Battery of the device should last multiple days (up to 1-2 weeks).
During the RAN1 102-e meeting, understanding on the peak data rate of wearable is aligned among companies, 2 possible understandings are listed as follows
  Option #1: Different wearables could support different peak data rates. Some high-end wearables can achieve the requirement of up to 150Mbps in DL and up to 50Mbps in UL.
  Option #2: All wearables should achieve the same peak data rate, which can be the same or lower than 150Mbps in DL and 50Mbps in UL.
  RAN1 progress has been delayed due to controversial views

## Slide 3: Background#2
From the market perspective, such high peak data rate (150Mbps in DL, 50Mbps in UL) is not needed in most use cases such as smart watches, rings, health sensors , etc.,
The typical data rate requirement for these “low-end” wearables is similar to that of LTE cat-1bis
  Peak data rate: 10Mbps in DL and 5Mbps in UL
Requiring all the wearable devices to have the capability of achieving up to 150Mbps in DL and up to 50Mbps in UL is not cost-efficient and power-efficient
In RAN#88e, Xiaomi and many companies cosign the RP-200946 lead by vivo to clarify the SID justification section for wearables that for low-end wearables, 150Mbps in DL and up to 50Mbps in UL is not mandatory.

## Slide 4: Proposal
Proposal #1: Clarify the understanding of the peak data rate for wearables to avoid the ambiguity understanding
Proposal#2: revise the SID as following:
  Wearables: Reference bitrate for smart wearable application can be 5-50 Mbps in DL and 2-5 Mbps in UL and peak bit rate of the device higher, up to 150 Mbps for downlink and up to 50 Mbps for uplink. Battery of the device should last multiple days (up to 1-2 weeks).
  Note: Not all Redcap devices are mandated to support the same peak data rate.

## Slide 5
Thank you