## Slide 1: Motivation for Study on high power UE (power class 2) for one NR FDD band
China Unicom, Huawei, HiSilicon
3GPP TSG RAN meeting #89e RP-201645
Electronic Meeting, September 14-18, 2020

## Slide 2: Background
RAN4 has standardized NR TDD PC2 HPUE feature for 5G SA deployments in NR bands n41, n77, n78 and n79 in R15 to improve NR uplink coverage, and both PC2 UL MIMO (2Tx 23+23dBm) and PC2 1Tx (26dBm) UE are supported.
RAN4 has standardized EN-DC HPUE feature for 5G NSA deployments in R16. And FDD band could also support high transmit power. The following EN-DC band combination support for power class 2:
  DC_39A_n41A, DC_39C_n41A, DC_39A_n79A, DC_41A_n79A, DC_41C_n79A, DC_3A_n78A, DC_3A_n41A
For NR FDD band, e.g. max bandwidth of n1 is 50MHz，meanwhile it is 20MHz for LTE band b1. Currently, the maximum total transmission power for NR FDD band is same as LTE FDD bands as 23dBm. The uplink transmission power is not enough for NR if considering the same requirements of PSD.

## Slide 3: Motivation
Benefits of Introducing NR FDD HPUE
  FDD is rich in low-/middle-frequency bands, which has the advantage of good cell coverage for both uplink and downlink. If considering NR deployment, NR FDD band will extend the uplink coverage for 5G subscriber.
    For commercial deployment scenario, indoor digital distribution systems are not always available for building scenarios, consequently, this will lead to the poor indoor coverage due to extra penetration loss when signals transmits from outdoor to indoor.
  There would be potential benefits for introducing NR FDD HPUE(PC2) to improve the cell capacity and subscriber’s performance.
Some initial simulation result are provided for evaluating the benefits of introducing NR FDD HPUE(PC2)
  Increment of transmission power of UE will greatly improve the spectrum efficiency for uplink throughput (UPT) for both cell average and cell edge .
Antenna | Max Tx power/dBm | Packet size | Packet arrival rate | Cell avg. UPT gain | 5% UPT gain
BS: 4R UE: 1T | 23 | 100k Byte | 1 file/s | 0%,baseline | 0%, baseline
BS: 4R UE: 1T | 26 | 100k Byte | 1 file/s | 81.54% | 71.05%
BS: 4R UE: 1T | 23 | 10k Byte | 1 file/s | 0%, baseline | 0%, baseline
BS: 4R UE: 1T | 26 | 10k Byte | 1 file/s | 97.16% | 87.41%

## Slide 4: Motivation
Some initial simulation result are provided for evaluating the benefits of introducing NR FDD HPUE(PC2)
  The performance gain on cell average throughput is obvious, and performance gains on 5% cell-edge rate is not so much because the scheduling period in one radio-frame is assumed to be limited up to 50%. But the spectrum efficiency for both cell average and cell-edge is greatly improved.
Antenna | Max Tx power/dBm | Packet size | Packet arrival rate | Cell avg. UPT/Mbps | 5% UPT/Mbps | Cell avg. UPT gain | 5% UPT gain
BS: 4R UE: 1T | 23 | 100k Byte | 1 file/s | 29.580 | 1.028 | 0%, baseline | 0%, baseline
BS: 4R UE: 1T | 26 | 100k Byte | 1 file/s | 44.611 | 1.034 | 50.81% | 0.52%
BS: 4R UE: 2T | 26 | 100k Byte | 1 file/s | 44.620 | 1.153 | 50.84% | 12.10%
BS: 4R UE: 1T | 23 | 10k Byte | 1 file/s | 5.972 | 1.212 | 0%, baseline | 0%, baseline
BS: 4R UE: 1T | 26 | 10k Byte | 1 file/s | 9.658 | 1.290 | 61.70% | 6.43%
BS: 4R UE: 2T | 26 | 10k Byte | 1 file/s | 9.701 | 1.291 | 62.44% | 6.51%

## Slide 5: New SID for Study on high power UE (PC2) for one NR FDD band
Based on the analysis and simulation results, it is proposed
  A new study item on PC2 UE for one NR FDD band(e.g. n1, max bandwidth is up to 50MHz) in RAN4.
Objectives
  Study the applicable scheme(s) for new power class 2 UE for one NR FDD band to comply with the SAR limits with 26dBm UE Tx power, the example band for this study is NR band n1.
  Study interference issues (e.g. self-desense, cross device coexistence…).
  Study the possible UE implementations, e.g. RF front-end capability, UE architectures, etc., in achieving 26dBm in FDD bands.

## Slide 6: Annex: Simulation Assumptions
Configuration parameters | Values
Scenario | Urban macro
ISD | 500 m
Duplexing | FDD
Carrier frequency | 2.1 GHz
Modulation | Up to 256QAM
Numerology | 15 kHz
Simulation bandwidth | 40 MHz
Transmission scheme | SU-MIMO
Codebook | For 2Tx, codebook [1 1]T is used for transmit diversity
SU dimension | Up to 1 layer
Antenna configuration at TRxP | 4Rx, (M,N,P,Mg, Ng) = (1,2,10,1,1; 1,2)
Antenna configuration at UE | 1Tx, (M,N,P,Mg, Ng) = (1,1,1,1,1; 1,1), 2Tx, (M,N,P,Mg, Ng) = (1,1,2,1,1; 1,1),
UE maximal transmit power | For 1Tx, 23 dBm for each TXRU For 1Tx, 26 dBm for each TXRU (High power UE) For 2Tx, 23 dBm for each TXRU (High power UE)
Scheduling | PF
Receiver | MMSE-IRC
Channel estimation | Ideal
Power control parameter | P0=-60, alpha = 0.6
TRxP number per site | 3
TRxP number | 21
Channel model | 38.901
Electronic tilt | 102°
Traffic model | FTP3, packet size: 100 kbyte / 10 kbyte, arrival rate: 1 packet / s.